## Slide 1: Autonomous Cyber-Physical Systems: Timed Models
Fall 2024. CSCI 513.
Instructor: Jyo Deshmukh
Acknowledgment: Some of the material in these slides is based on the lecture slides for CIS 540: Principles of Embedded Computation taught by Rajeev Alur at the University of Pennsylvania. http://www.seas.upenn.edu/~cis540/

## Slide 2: Models of Computation
[1] Nicolescu, Gabriela; Mosterman, Pieter J., eds. (2010). Model-Based Design for Embedded Systems. Computational Analysis, Synthesis, and Design of Dynamic Systems. 1. Boca Raton: CRC Press.
Synchronous Process Models
Asynchronous Process Models
Timed Models
  Like Asynchronous models, but with explicit time information
  Can make use of global time for coordination
Continuous-time models/Dynamical system models
  Like Synchronous, but time evolves continuously
Hybrid Dynamical Models

## Slide 3: Timed ESMs
Like asynchronous ESMs, have input, output channels, state variables
Special type of state variable called “clock”
Clock variables evolve continuously in time
ESM can “stay” in a mode with clock increasing monotonically from the start value
off
dim
bright
(press==1)?
c:=0
(press==1)?
clock c:=0
(press==1)? (c1)
(press==1)? (c1)

## Slide 4: Transitions of a timed ESM
Mode switch: discrete action
  machine moves from one mode to another
  guard on the transition must be true for mode switch to occur
  update specified by the transition will update/reset clock variables
off
dim
bright
(press==1)?
c:=0
(press==1)?
clock c:=0
(press==1)? (c1)
(press==1)? (c1)
(off,0.5)
(dim,0)
(press==1)?

## Slide 5: Transitions of a timed ESM
In a mode: Timed action
When machine stays in any given mode for time each clock variable increases by and all other state variables remain unchanged
Captures timing constraints
  Resetting c to 0 from offdim and guard c1 from dimoff specifies that these mode switches are 1 second apart
off
dim
bright
(press==1)?
c:=0
(press==1)?
clock c:=0
(press==1)? (c1)
(press==1)? (c1)

## Slide 6: Timed Processes: explicit clock variables
Clock variables
  Like other state variables, can be used in guards
  Can be reset to 0 during mode switches
  When the machine is in a given mode for duration the clock variable increases by
off
dim
bright
(press==1)?
c:=0
(press==1)?
clock c:=0
(press==1)? (c1)
(press==1)? (c1)

## Slide 7: Timed Process Execution
off
dim
bright
(press==1)?
c:=0
(press==1)?
clock c:=0
(press==1)? (c1)
(press==1)? (c1)
(off,0)
(off,0.5)
(dim,0)
(press==1)?
(dim,0.8)
(press==1)?
(bright,0.8)
Machine execution is through alternating timed transitions and mode switches

## Slide 8: Timed Process Execution
off
dim
bright
(press==1)?
c:=0
(press==1)?
clock c:=0
(press==1)? (c1)
(press==1)? (c1)
(off,0)
(off,0.5)
(dim,0)
(press==1)?
(dim,3.8)
Machine execution is through alternating timed transitions and mode switches
(press==1)?
(off,3.8)

## Slide 9: Timed Buffer
Input channel in of type bool
Output channel out of type bool
State variable x of type bool+. The value indicates empty
If x is , then read new value into x, and set clock to 0
If clock value is seconds, output value of x, and set x to
bool
out
bool in
x:= , clock c:=0
Tin (x==) & in?
x:=in; c:=0;
Tout (c2)
{ out := x;
x := }
Tinfull in?

## Slide 10: Timed State Machine representation
Mode captures whether x==
Clock variable tracks the time that elapsed since x received a value
Guard ensures that at least 2 seconds pass before the value of x is output
Guard does not force transitions
  can keep increasing while process remains in mode full
How do we make sure that process does not remain in full mode for at most 3 seconds?
empty
full
c out:=x, x≔
in? x:=in, c:=0
c:=0
in?

## Slide 11: Clock invariants
Attempt 1: we could make the guard
Attempt 1 fails because:
  You could keep getting new input (self-loop executes) till
Larger problem: Guards are non-forcing: nothing requires the guard to be executed
We can fix this by introducing clock invariants
Clock invariant of any mode: symbolic expression that must evaluate to true at all times, and if not, the process must exit that mode
empty
full
c out:=x, x≔
in? x:=in, c:=0
c:=0
in?

## Slide 12: Clock invariants
Add clock invariant:
(mode==full) (c 3)
Forces process to leave mode full if c becomes greater than 3
Staying in mode full when c would violate the clock invariant
Useful construct to limit how long a process stays in a certain mode
empty
full
c
c out:=x, x≔
in? x:=in, c:=0
c:=0
in?

## Slide 13: Why model using invariants and guards?
Each mode is a guard-enabled task; if guard is true, task is executed
  Going from one mode to another is a task switch
Checking if process leaves mode and goes to depends on if incoming guard of is true
Staying in does not/should not depend on the guard of
So, we use invariants:
  a condition always checked in a given mode
mode , clock

## Slide 14: Example with two clocks
Model with one input channel and two output channels: out1 and out2
Clock c tracks time elapsed since occurrence of the input task execution
Clock d tracks time elapsed since occurrence of output task for out1
Behavior of process: If input event occurs at some time t, then process issues output # on out1 some time t’ [t,t+1] and then issues output * on out2 at time t’’ [t’+1, t+2]
wait1
c1
idle
Wait2
c2
clock c,d:=0
in? c:=0
out1!#;d:=0
d
out2!*

## Slide 15: Formal recap of a timed process
Timed process consists of:
  An asynchronous process, where some of the state variables are of type clock (ranging over non-negative reals)
  A clock invariant I which is a Boolean expression over the state variables
Inputs, Outputs, States, Initial states, Actions: Internal, Input and Output: same as for asynchronous processes
Timed Action: Given a state q and time , action q q’ specifies a transition of duration if:
  q’ represents a state where the non-clock variables have the same value as in q, i.e. q’(x) = q(x)
  q’ represents a state where the clock variables in q are incremented by , i.e. q’(c) = q(c) + and
  For all times t [q(c), q(c)+], the clock invariant I is satisfied
  If clock invariant is convex, enough to check clock invariant at q(c) and q(c)+

## Slide 16: Composing Timed Processes
empty
full
c1
c1B1 out1:=x1, x1≔
in? x1:=in, c1:=0
c1:=0
empty
full
c2
c2B2 out2:=x2, x2≔
in? x2:=in, c2:=0
c2:=0
Each process stays in mode full for
Need to construct a new process with 4 new modes
Each new mode is a pair consisting of modes from process 1 and 2
Mode switches in the new machine correspond to mode switches in the old machine
Interesting timing behavior can arise!

## Slide 17: Composing Timed Processes
empty
full
c1 A1
c1B1 out1:=x1
in? x1:=in, c1:=0
c1:=0
empty
full
c2 A2
c2B2 out2:=x2
in? x2:=in, c2:=0
c2:=0
in?
in?
empty,
empty
full, empty
c1A1
empty, full
c2A2
full,full
c1A1
c2A2
c1B1 out1:=x1
c1B1 out1:=x1
in?
in?
c2B2 out2:=x2
c2B2 out2:=x2
in? x1:=in, c1:=0,
x2:=in, c2:=0
in? x1:=in, c1:=0

## Slide 18: Semi-synchrony
If B1 A1 B2 :
(full,full) (full,empty) can never be enabled!
Why?
reaches and the process gets kicked out of state (full,full)
But cannot be greater than so, guard from (full,full) to (full,empty) is not enabled!
empty,
empty
full, empty
c1A1
empty, full
c2A2
full,full
c1A1
c2A2
c1B1 out1:=x1
c1B1 out1:=x1
in?
in?
c2B2 out2:=x2
c2B2 out2:=x2
in? x1:=in, c1:=0,
x2:=in, c2:=0
in? x1:=in, c1:=0

## Slide 19: Semi-synchrony
If B1 A1 B2 :
  (full,full) (full,empty) cannot happen
If B1 A1 B2 :
  (full, full) (empty,full) will happen eventually
out1 guaranteed to happen before out2
Implicit coordination based on delays
  Both process clocks increase in tandem
  Global clock-based synchronization
Reason why timed models are called semi-synchronous or partially synchronous
empty,
empty
full, empty
c1A1
empty, full
c2A2
full,full
c1A1
c2A2
c1B1 out1:=x1
c1B1 out1:=x1
in?
in?
c2B2 out2:=x2
c2B2 out2:=x2
in? x1:=in, c1:=0,
x2:=in, c2:=0
in? x1:=in, c1:=0

## Slide 20: Pacemaker Modeling as a Timed Process
Most material that follows is from this paper:
Z. Jiang, M. Pajic, S. Moarref, R. Alur, R. Mangharam, Modeling and Verification of a Dual Chamber Implantable Pacemaker, In Proceedings of Tools and Algorithms for the Construction and Analysis of Systems (TACAS), 2012.
Alur’s textbook has detailed descriptions of some other pacemaker components

## Slide 21: How does a healthy heart work?
SA node (controlled by nervous system) periodically generates an electric pulse
This pulse causes both atria to contract pushing blood into the ventricles
Conduction is delayed at the AV node allowing ventricles to fill
Finally the His-Purkinje system spreads electric activation through ventricles causing them both to contract, pumping blood out of the heart
Electrical Conduction System of the Heart

## Slide 22: What do pacemakers do?
Aging and/or diseases cause conduction properties of heart tissue to change leading to changes in heart rhythm
Tachycardia: faster than desirable heart rate impairing hemo-dynamics (blood flow dynamics)
Bradycardia: slower heart rate leading to insufficient blood supply
Pacemakers can be used to treat bradycardia by providing pulses when heart rate is low

## Slide 23: Implantable Pacemaker modeling

## Slide 24: How dual-chamber pacemakers work
Two fixed leads on wall of right atrium and ventricle respectively
Activation of local tissue sensed by the leads (giving rise to events Atrial Sense (AS) and Ventricular Sense (VS))
Atrial Pacing (AP) or Ventricular Pacing (VP) are delivered if no sensed events occur within deadlines
Heart
Pacemaker
AS
VS
AP
VP

## Slide 25: The LRI mode of operation explained
ASed
LRI
c K
VP? c:=0
VS? c:=0
AS?
VS? c:=0
VP? c:=0
c K AP!; c:=0
K= 850ms
LRI = lower rate interval
LRI component keeps heart rate above minimum level
One of the pacemaker modes of operation that models the basic timing cycle
Measures the longest interval between ventricular events
Clock reset when VS or VP received
No AS received LRI outputs AP after K time units

## Slide 26
Finite State Automata: A 3-slide introduction

## Slide 27: Finite state automata
Famous equivalence between finite state automata and regular expressions
a-z
a-z,0-9
[a-z][a-z 0-9 ]
a-z
a-z
0-9
[a-z][0-9]*[a-z]
State
Accepting
state
*
0-9

## Slide 28: How does a finite state automaton work?
Starts at the initial state
In , if it receives a letter in a-z, goes to
  else, it goes to
In , if it receives a number in 0-9, it stays in
else, it goes to (as it received a-z)
In , no matter what it gets, it stays in
is an accepting state where computation halts
Any string that takes the machine from to is accepted by the machine
a-z
a-z
0-9
*
0-9

## Slide 29: Language of a finite state automaton
What strings are accepted by ?
  ab, zy, s2r, q123s, u3123123v, etc.
What strings are not accepted by ?
  2b, 334a, etc.
The set of all strings accepted by is called its language
The language of a finite state automaton consists of strings, each of which can be arbitrarily long, but finite
a-z
a-z
0-9
*
0-9

## Slide 30: Timed Automata
Useful tool to do timing analysis and explore properties of timed processes
State-space of timed automata is infinite (clocks can become arbitrarily large!)
But some questions about timed automata behavior can still be answered exactly
  Does the automaton accept any string? (also known as emptiness problem)
  Reachability of a particular configuration
We will revisit this later in the course

## Slide 31: Timing Analysis
x>=3  y:=0
A
x<=5
(y >= 6)?
(x = 7)?
x,y:=0
(y >= 2)?
B
x<=7
C
x8
y 5
(x <= 4)?
D
E
F
Which of D, E, F can be reached?
Needs careful propagation of reachable combinations of x and y
x , y when we reach B
x y when we reach C
x , y when you exit C
OR x y and machine stops

## Slide 32: How is such analysis done?
The key challenge is that if the automata has loops, then how do we know that our procedure for propagation of symbolic clock constraints will terminate?
The key insight by first papers on timed automata was that there is only a finite number of regions in the clock-space that can be visited
This gives a “pumping lemma” style argument*
Allows abstracting a finite timed automaton to an automaton where modes/states represent the regions
This was expensive, and improved by using zone-based constructions
  (zones are a uniform representation of constraints that arise during analysis)