## Slide 1: Autonomous Cyber-Physical Systems: Multi-Agent Systems
Fall 2025. CS 513.
Instructor: Jyo Deshmukh
USC Viterbi
School of Engineering
Department of Computer Science

## Slide 2: Multi-agent Systems: Taxonomies
Structural:
  Hierarchical: Layered agents with supervision
  Distributed: Fully decentralized peers
  Modular: Loosely coupled modules
Coordination:
  Centralized: one controller governs behaviors of all agents (good for warehouses)
  Decentralized: each agent coordinates based on its sensors and rules (e.g. exploration)
  Consensus-based: agreement via iterative negotiation
  Market-based: common resources/tasks traded by agents
Dynamics & Interaction
  Cooperative: Agents pursue share goals
  Competitive: Agents are self-interested
  Coalitional: Agents form coalitions to pursue goals
  Swarm systems: Large groups with simple rules

## Slide 3: Multi-agent autonomous systems
Networks of vehicles
Drone swarms for biological applications, surveillance, environment monitoring
Military applications
Warehouse robots
Industrial manufacturing robots
IoT systems

## Slide 4: Basic Model for Consensus
Nodes:
Edges:
Neighbors of node
: value of node
: Algebraic graph/Network
  value
  topology or information flow
Olfati-Saber, Reza, and Richard M. Murray. "Consensus problems in networks of agents with switching topology and time-delays." IEEE Transactions on automatic control 49, no. 9 (2004): 1520-1533.

## Slide 5: Some neat things from algebraic graph theory
Laplacian matrix of a graph defined as:
If graph is weighted replace 1 with the weight of that edge
Multiplicity of the zero eigenvalue of the matrix is the number of components of the graph (nodes that can be reached from each other)
Speed of convergence of algorithms for flocking, rendezvous, consensus depend on the second smallest eigenvalue of the Laplacian matrix

## Slide 6: Consensus
Nodes and agree iff
Nodes of a network have reached consensus iff
Common value of all nodes is called “group decision value”
Dynamic graph : Dynamical system in which evolves according to dynamics function where

## Slide 7: -consensus problem
L be a function of
is an initial state of the system, then
-consensus problem is to calculate by applying inputs that only depend on and the neighbors of
is called a protocol with topology if:
  the cluster satisfies the property that
  i.e., if the feedback only uses a node and some subset of its neighbors
above is called a distributed protocol: if

## Slide 8: Solving the -consensus problem
Protocol solves the -consensus problem iff there exists an asymptotically stable equilibrium of satisfying for all
Some special cases:
  Max-consensus:
  Min-consensus:
  Average-consensus:

## Slide 9: Example of a consensus protocol
Imagine a network of agents with integrator dynamics
Protocol 1: (neighbors can be fixed or can change):
Protocol 2: (with time delay for each )

## Slide 10: Challenge problems in consensus
Different kinds of topologies
Different assumptions on structures of the graphs
Types of problems to solve (min/max/average)
How do you prove that the consensus algorithm actually converges?
  Requires ideas similar to Lyapunov functions
  Called disagreement functions that show that disagreement decreases over time
Olfati-Saber, Reza, and Richard M. Murray. "Consensus problems in networks of agents with switching topology and time-delays." IEEE Transactions on automatic control 49, no. 9 (2004): 1520-1533.

## Slide 11
Vehicle to Vehicle (V2V) and Vehicle to Everything(V2X)

## Slide 12: V2V algorithms
Forward crash avoidance
Cooperative Adaptive Cruise Control
Cooperative Collision Avoidance
Cooperative Merging
https://www.its.dot.gov/research_archives/safety/v2v_comm_safety.htm

## Slide 13: Cooperative Adaptive Cruise Control (CACC)
Used for platoons of vehicles (e.g., trucks)
Several goals:
  Improve safety
  Improve traffic flow dynamics by damping disturbances (new cars, braking, bumps in the road)
  Increasing highway capacity by shorter following gaps
  Saving energy and pollution through aerodynamic drafting
  Improving driver comfort and convenience

## Slide 14: CACC uses different gap regulation strategies
Constant clearance or constant distance gap (CDG)
  Separation does not change with vehicle velocity
  Gives experience of mechanical linkage between vehicles
  Requires more formal platoon architecture and tight communication between platoon leader and followers
  Communication interruption can cause safety hazards
  Need larger gaps to ensure safety of platoon
  (Emergency brake by leader can cause domino effect)

## Slide 15: CACC uses different gap regulation strategies
Constant Time Gap
  Resembles how normal human drivers drive
  Distance between vehicles is proportional to their speed + a small fixed offset distance
  E.g., doubling of speed causes doubling of gap between vehicles
  Time gap criterion described in terms of time between rear bumper of leading vehicle and front bumper of trailing vehicle pass a fixed point on the roadway
  Often described as headway or time headway
  Vehicles in CTG CACC are often called a “string of vehicles” rather than platoon

## Slide 16: CACC string splits and faults
CACC needs to handle trucks leaving string
Ideally, departing truck signals intent and remaining string close gaps to maintain platoon structure
In some cases, may require string to be split while the truck in the middle departs
Protocols have NUMEROUS fault conditions, errors and abnormal operating conditions (obstacle in the road, accidents, etc.)
Safety: model each truck as an asynchronous process and reason about composition of asynchronous processes!
Specifications: Safety and String stability

## Slide 17: Autonomous Intersection Management
AIM protocol and its variants proposed based on V2I communication
Main idea :
  Each car equipped with a driver agent
  Each intersection equipped with an intersection manager
  Driver agents call ahead to reserve space-time in an intersection
  Intersection manager decides to grant or reject reservation requests according to an intersection control policy

## Slide 18: AIM protocol4
Approach vehicle announces arrival to manager
Vehicle indicates its size, predicted arrival time, velocity, acceleration, arrival and departure lanes
Intersection manager simulates vehicle’s path through the intersection, checking for conflicts with paths of previously processed vehicles
If there are no conflicts, issues a reservation
It is the vehicle’s responsibility to arrive at and travel through the reserved space-time block within some range of error tolerance
In case of conflict, intersection manager suggests an alternate later reservation
Car enters intersection only if reservation successful
Upon leaving intersection, car conveys successful passage to the manager

## Slide 19: Intersection control policies
Divide intersection into grid of reservation tiles

## Slide 20: Collaborative merge
Purpose: allow vehicles merging onto a freeway from a ramp to do so in safe fashion
Can be formulated as a specific case in AIM
Specialized approaches based on highway ramp metering have existed for some time (do not utilize V2V, do not guarantee safety)

## Slide 21: Reasoning about Multi-Agent Systems with Logic
STL-based approaches:
  Define predicates between pairs of agents, predicates on states of each agent
Spatio-Temporal Logic-based approaches
  STREL: (Spatio-Temporal Reach & Escape Logic)
    Over undirected graphs, uses one dynamic graph topology
  STL-GO: (STL + Graph Operators)
    Over directed graphs, can have multiple underlying graph topologies and graph operators to choose among topologies
    Spatial operators over incoming and outgoing neighbors

## Slide 22: MAS: dynamic graph structures
Graph structure
  Sensing graph
  Visibility Graph
  Communication Network
Agents have:
  temporally evolving state
  spatial location
STREL
  Logic defined over spatially distributed agents
  Evaluated over a spatial model
  Spatial model: time-varying graph with temporally evolving nodes

## Slide 23: STREL Syntax
STREL formulas:
Evaluated at a given node in a spatial model
Includes STL (allowing monitoring of time-varying behaviors)
Includes Spatial Operators (here are arbitrary STREL formulas)

## Slide 24: STREL example: Somewhere/Everywhere
Agents:
  Ego = black
  Links may disappear!
  Agents move!
  is satisfied by because is within hops at time , and it reaches green within seconds
  is satisfied by because within seconds, all its 1-hop neighbors are not yellow

## Slide 25: STREL example: Reach and Escape
is satisfied because there is a route of length where along the route holds before Red is reached.
is satisfied because there is a route of length where along the route

## Slide 26: STREL examples
Drone flocking with several obstacles
STREL formulas1:
  For each drone there is a connected drone within 2 hops or within 100 seconds, there is either a drone or a base station within 2 hops
  Always, the drone does not collide with obstacles, and the drone remains within 2 hops of a ground station until it reaches its goal location
1. A. Balakrishnan, S. Paul, S. Silvetti, L. Nenzi, J. Deshmukh, Monitoring Spatially Distributed CPS with Alternating Finite Automata, HSCC 2025, Best Paper Award

## Slide 27: References
[1] Shladover, Steven E., et al. "Cooperative adaptive cruise control: Definitions and operating concepts." Transportation Research Record: Journal of the Transportation Research Board 2489 (2015): 145-152.
[2] ibid., https://escholarship.org/uc/item/7jf9n5wm
[3] Liang, Chi-Ying, and Huei Peng. "String stability analysis of adaptive cruise controlled vehicles." JSME International Journal Series C Mechanical Systems, Machine Elements and Manufacturing 43.3 (2000): 671-677.
[4] Stone, Peter, Shun Zhang, and Tsz-Chiu Au. "Autonomous intersection management for semi-autonomous vehicles." Routledge Handbook of Transportation. Routledge, 2015. 116-132.
[5] Qian, Xiangjun, et al. "Autonomous Intersection Management systems: criteria, implementation and evaluation." IET Intelligent Transport Systems 11.3 (2017): 182-189.
[6] de Campos, Gabriel Rodrigues, et al. "Traffic coordination at road intersections: Autonomous decision-making algorithms using model-based heuristics." IEEE Intelligent Transportation Systems Magazine 9.1 (2017): 8-21.
[7] Rios-Torres, Jackeline, and Andreas A. Malikopoulos. "A survey on the coordination of connected and automated vehicles at intersections and merging at highway on-ramps." IEEE Transactions on Intelligent Transportation Systems 18.5 (2017): 1066-1077.