## Slide 1: Autonomous Cyber-Physical Systems: Requirements, Linear Temporal Logic
Fall 2025. CS 513.
Instructor: Jyo Deshmukh

## Slide 2: Where we are in the course
Done with Module 1!
Module 1: Models of Computation + Control
Module 2: Formal Specification, Verification, Testing

## Slide 3: Module 2 : Formal Specification, Verification, Testing
Formal Requirements/Specifications
Requirements-based Testing
Safety Verification

## Slide 4: Requirements
Requirements: describe desirable properties of system behaviors
High assurance/safety-critical, or mission-critical systems must use formal requirements
Behavioral requirements: requirement can be evaluated on individual system behaviors
Requirements met by system if all behaviors satisfy requirements
There needs to be a clear separation between requirements (what needs to be implemented) and the design (how should it be implemented)
Unfortunately, this is not often obeyed

## Slide 5: Rigor in Requirements
Informal requirements: implicit or stated in natural language
  If an obstacle is sensed by the car, it should stop if it is safe to do so
Formal requirements: explicit and mathematically precise
  If the vision system with a probability
    labels an object meters from the car as a stationary obstacle,
  Then
    if current velocity of the car is less than ,
      vehicle should execute an emergency stop maneuver within ms.
Here, the maximum braking deceleration that the car can produce at velocity is , and is a safe stopping distance between vehicles

## Slide 6: Granularity
Granularity of requirements
  System-level: UAV is able to maintain a given desired altitude in presence of acceptable disturbances.
  Subsystem-level: Upon receiving a ‘turn right’ command, flight control subsystem (FCS) produces the correct actuator commands that cause the UAV to turn right.
  Function-level: For the position controller module, the maximum error between the estimated position and the position setpoint is less than 5%.
  Hardware/Timing-level: The MPC algorithm for attitude control has a worst-case execution time of 4 ms.

## Slide 7: Types of Requirements
Hard Requirements: Violation leads to endangering safety-criticality or mission-criticality
  Safety Requirements: system never does something bad
  Liveness Requirements: from any point of time, system eventually does something good
Soft Requirements: Violations lead to inefficiency, but are not critical
  (Absolute) Performance Requirements: system performance is not worse than a certain level
  (Average) Performance Requirements: average system performance is at a certain level

## Slide 8: Nonfunctional/non-behavioral requirements
Security Requirements: system should protect against modifications in its behavior by an adversarial actor
  Failure to satisfy security requirements may lead to a hard requirement violation
Privacy Requirements: the data revealed by the system to the external world should not leak sensitive information
These requirements will become increasingly important for autonomous CPS, especially as IoT technologies and smart transportation initiatives are deployed!

## Slide 9: Requirement Formalisms
Languages and Logics to describe mathematically precise requirements
Examples:
  Automata, State Machines
  Propositional Logic, Temporal Logic, Regular Expressions
  Structured language/grammar-based requirements

## Slide 10: Propositional Logic
Simplest form of logic with a set of atomic propositions and Boolean connectives
, Connectives =
Syntax recursively gives how new formulae are constructed from smaller formulae
Syntax of Propositional Logic |  |  | 
 |  | ¦ | the true formula
 |  | ¦ | is a prop in AP
 |  | ¦ | Negation
 |  | ¦ | Conjunction
 |  | ¦ | Disjunction
 |  | ¦ | Implication
 |  | ¦ | Equivalence
Syntax of Propositional Logic |  |  | 
 |  | ¦ | the true formula
 |  | ¦ | 
 |  | ¦ | Negation
 |  | ¦ | Conjunction
 |  | ¦ | Disjunction
 |  | ¦ | Implication
 |  | ¦ | Equivalence

## Slide 11: Semantics
Semantics (i.e. meaning) of a formula can be defined recursively
Semantics of an atomic proposition defined by a valuation function
Valuation function assigns each proposition a value 1 (true) or 0 (false), always assigns the formula the value 1, and for other formulae is defined recursively
Semantics of Prop. Logic | 
 | 1
 | 1 if 0 if
 | 1 if = 1 and , 0 otherwise
Semantics of Prop. Logic | 
 | 1

## Slide 12: Examples
: There is an upright bicycle in the middle of the road
: There is car in the field of vision
: If there is an upright bicycle in the middle of the road, the bicycle has a rider
Car is in the intersection

## Slide 13: Interpreting a formula of prop. logic
. What is
= 1
. What is
= 0
Is this true? = 1? (For all valuations)?

## Slide 14: Temporal Logic
Temporal Logic (literally logic of time) allows us to specify finite and infinite sequences of states using logical formulae
An -language is a set of sequences, each of which is possibly infinite in length, temporal logics help specify many interesting classes of -languages
Temporal logic grew out of philosophy: tense logic and modal logic
Amir Pnueli in 1977 used a form of temporal logic called LTL for requirements of reactive systems: later selected for the 1996 Turing Award
LTL is now adopted by the industry (part of Property Spec. Language, which is an IEEE standard), is supported by many tools in the EDA/CAD industry

## Slide 15: Temporal Logic = Prop. Logic + Temporal Operators
Propositional Logic is interpreted over valuations to atoms
Temporal Logic is interpreted over traces/sequences/strings
Trace is an infinite sequence of valuations
0
1
2
3
4
42
Can also write as: (0,1,1), (1,1,0), (2,0,0), (3,1,1),(4,0,1),… ,(42,1,1), …

## Slide 16: Linear Temporal Logic
LTL is a logic interpreted over infinite traces
Temporal logic with a view that time evolves in a linear fashion
  Other logics where time is branching!
Assumes that a trace is a discrete-time trace, with equal time intervals
Actual interval between time-points does not matter : similar to rounds in synchronous reactive components
LTL can be used to express safety and liveness properties!

## Slide 17: LTL Syntax
LTL formulas are built from propositions and other smaller LTL formulas using:
  Boolean connectives
  Temporal Operators
Only shown and , but can define for convenience
Syntax of LTL |  |  | 
 |  | ¦ | is a prop in AP
 |  | ¦ | Negation
 |  | ¦ | Conjunction
 |  | ¦ | NeXt Step
 |  | ¦ | Some Future Step
 |  | ¦ | Globally in all steps
 |  | ¦ | In all steps Until in some step
Syntax of LTL |  |  | 
 |  | ¦ | 
 |  | ¦ | Negation
 |  | ¦ | Conjunction
 |  | ¦ | NeXt Step
 |  | ¦ | Some Future Step
 |  | ¦ | Globally in all steps
 |  | ¦ | In all steps Until in some step

## Slide 18: LTL Semantics
Semantics of LTL is defined by a valuation function that assigns to each proposition at each time-point in the trace a truth value (0 or 1)
We use the symbol (read models) to show that a trace-point satisfies a formula
: Read as trace at time satisfies formula
If we omit , then the meaning is time 0. I.e. is the same as
Semantics is defined recursively over the formula
Base case: Propositional formulas, Recursion over structure of formula

## Slide 19: Recursive semantics of LTL: I
if ,
  i.e. if is true at time
if ⊭ ,
  i.e. if is not true for the trace starting time
if and
  i.e. if and both hold starting time
if
  i.e. if holds starting at the next time point

## Slide 20: Recursive semantics of LTL: II
if such that
  i.e. is true starting now, or there is some future time-point from where is true
if :
  i.e. is true starting now, and for all future time-points , is true starting at
if s.t. and s.t. ,
  i.e. eventually holds, and for all positions till holds, holds

## Slide 21: Visualizing the temporal operators
: NeXt Step
0
1
2
3
4
42
: Some Future step
0
1
2
3
4
42
0
1
2
3
4
42

## Slide 22: Visualizing the temporal operators
: Globally holds
0
1
2
3
4
42
: holds Until holds
0
1
2
3
4
42

## Slide 23: You can nest operators!
What does mean?
  Trace satisfies (at time 0) if at time 1, holds. I.e. holds at some point strictly in the future
0
1
2
3
4
42
What does mean?
  Trace satisfies (at time 0) if at , there is always a in the future
0
1
2
14
15
65

## Slide 24: More operator fun
What does mean?
10
11
12
13
14
42
0
What does mean?
0
1
2
14
15
65
54

## Slide 25: More, more operator fun
What does the following formula mean: ?
0
1
2
3
4
5
Is this true? is the same as ?
0
1
2
3
4
42
No! Because this trace satisfies , but not

## Slide 26: Operator duality and identities

## Slide 27: Example specifications
Suppose you are designing a robot that has to do a number of missions
Kitchen
Bedroom
Living Room
Bathroom
Study
Whenever the robot visits the kitchen, it should visit the bedroom after.
Robot should never go to the bathroom
The robot should keep working until its battery becomes low
The robot should repeatedly visit the living room
Whenever the TV is on and the living room has no person in it, then within three steps, the robot should turn off the TV
TV
Passage

## Slide 28: Example specifications in LTL
Suppose you are designing a robot that has to do a number of missions
Whenever the robot visits the kitchen, it should visit the bedroom after.
Robot should never go to the bathroom.
The robot should keep working until its battery becomes low
Kitchen
Bedroom
Living Room
Bathroom
Study
TV
Passage

## Slide 29: Example specifications in LTL
Suppose you are designing a robot that has to do a number of missions
The robot should repeatedly visit the living room
Whenever the TV is on and the living room has no person in it, then within three steps, the robot should turn off the TV
room occupied by a person
Kitchen
Bedroom
Living Room
Bathroom
Study
TV
Passage

## Slide 30: Detour to automata and formal languages
Most programmers have used regular expressions
Formally, regular expressions specify acceptable sequences of finite length
Example:
  [a-z][a-z 0-9] : strings starting with a lowercase letter (a-z) followed by one lowercase letter or number
  [a-z][0-9]*[a-z] : strings starting with a lowercase letter, followed by finitely many numbers followed by a lowercase letter

## Slide 31: Finite state automata
Famous equivalence between finite state automata and regular expressions
a-z
a-z,0-9
[a-z][a-z 0-9 ]
a-z
a-z
0-9
[a-z][0-9]*[a-z]
State
Accepting
state
*
0-9

## Slide 32: How does a finite state automaton work?
Starts at the initial state
In , if it receives a letter in a-z, goes to
  else, it goes to
In , if it receives a number in 0-9, it stays in
else, it goes to (as it received a-z)
In , no matter what it gets, it stays in
is an accepting state where computation halts
Any string that takes the machine from to is accepted by the machine
a-z
a-z
0-9
*
0-9

## Slide 33: Language of a finite state automaton
What strings are accepted by ?
ab, zy, s2r, q123s, u3123123v, etc.
What strings are not accepted by ?
2b, 334a, etc.
The set of all strings accepted by is called its language
The language of a finite state automaton consists of strings, each of which can be arbitrarily long, but finite
a-z
a-z
0-9
*
0-9

## Slide 34: Safety Requirements/Specifications
A safety requirement states that a system always stays within the set of good states (i.e. nothing bad every happens)
Examples:
  Collision avoidance: the distance between a car and a pedestrian is always greater than a threshold
  Patient’s blood glucose never drops below 80 mg/dL
  Maximum temperature specification on the battery is not exceeded
Safety requirements can be formalized using monitors
  Monitor issues an error whenever safety requirement is violated

## Slide 35: LTL Monitors
A safety monitor classifies system behaviors into good and bad
Can we use a monitor to classify infinite behaviors into good or bad?
Yes, using theoretical model of Büchi automata proposed by J. Richard Büchi in 1960

## Slide 36: Büchi automaton: Example 1
Extension of finite state automata to accept infinite strings
0
1
States :
Input variable with domain :
Final state:
Transitions: (as shown)
Given trace (infinite sequence of symbols from , is accepted by , if there exists a path from the initial state where appears infinitely often
1
0

## Slide 37: Büchi automaton Example 2
: , : :
Transitions: (as shown)
Note that this is a nondeterministic Büchi automaton
accepts if there exists a path along which a state in appears infinitely often
  Fun fact: there is no deterministic Büchi automaton that accepts this language

## Slide 38: Büchi automaton Example 3
What is the language of ?
Infinite strings where:
  Always when , in some future step,
  In other words, must be followed by
|
1 &
: , : :
Transitions: (as shown)

## Slide 39: Büchi automaton and LTL
Language of an automaton: set of all strings accepted by the automaton
0
1
What is the language of ?
LTL formula
1
0

## Slide 40: Büchi automaton Example 2
: , : :
Transitions: (as shown)
What is the language of ?
LTL formula

## Slide 41: Büchi automaton Example 3
What is the language of ?
LTL formula:
I.e. always when , in some future step,
In other words, must be followed by
|
1 &
: , : :
Transitions: (as shown)

## Slide 42: Using Büchi monitors
Theoretical result: Every LTL formula can be converted to a Büchi monitor/automaton
Size of is generally exponential in the size of ; blow-up unavoidable in general

## Slide 43: Büchi monitors for runtime monitoring
Runtime monitoring: return a verdict based on only a finite portion of the trace
Some kinds of formulas can be monitored on finite traces
Finitely satisfiable:
Finitely refutable:
Some formulas can never return a verdict on finite traces