## Slide 1: Autonomous Cyber-Physical Systems: Basics of Verification
Fall 2025. CS 513.
Instructor: Jyo Deshmukh

## Slide 2: Safety Requirements/Specifications
A safety requirement states that a system always stays within the set of good states (i.e. nothing bad every happens)
Examples:
  Collision avoidance: the distance between a car and a pedestrian is always greater than a threshold
  Patient’s blood glucose never drops below 80 mg/dL
  Maximum temperature specification on the battery is not exceeded
Safety requirements can be formalized using transition systems

## Slide 3: Transition System
Transition System is a tuple
  : Set of State Variables over finite or infinite domains
  : Function mapping to initial values
  : Transition description giving code to update variables in
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?

## Slide 4: Example of a TS
: { mode, x }
Semantics:
: { mode off, x 0 }
has an infinite number of transitions
  (off, 0) (off, 0)
  (off, 0) (on, 0)
  (on, n) (on, n+1) if n < 10
  (on, n) (off, 0) otherwise
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?

## Slide 5: Transition Systems and state
All kinds of components (synchronous, asynchronous, timed, hybrid, continuous components) have an underlying transition system
State in the transition system underlying a component captures any given runtime configuration of the component
Continuous components, Timed Processes, Hybrid Processes in general, have infinite number of states/transitions

## Slide 6: Example transitions for TS
(off,0)
(on,0)
(on,1)
(on,2)
(on,100)
(off,42)
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?
(on,42)

## Slide 7: TS describes all possible transitions
(off,0)
(on,0)
(on,1)
(on,2)
(on,100)
(off,42)
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?
(on,42)
Transitions indicated as dotted lines can’t really happen in the component
But the TS will describe then, as the states of the TS are over!

## Slide 8: Reachable states of a modified switch TS
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?
(off,0)
(on,0)
(on,1)
(on,2)
(on,100)
(off,42)
(on,42)
Reachable states and transitions

## Slide 9: Desirable behaviors of a TS
Desirable behavior of a TS:
  Defined in terms of acceptable (finite or infinite) sequences of states
  If all unacceptable sequences of a TS are finite in length, then the property encoding acceptable behavior is called a safety property
Safety property can be specified by partitioning the states into a safe/unsafe set
  , ,
  Any finite sequence that ends in a state is a witness to undesirable behavior, or if all (infinite) sequences starting from an initial state never include a state from , then the TS is safe.

## Slide 10: Safety invariants
An invariant is a Boolean expression over the state variables of a TS
A property is called an invariant of TS if every reachable state of TS satisfies
An invariant is a safety invariant if
Examples of invariants for modified switch:
  [note: is an int]
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?

## Slide 11: Safety invariants
Are the following invariants?:
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?

## Slide 12: Proofs of Safety
Suppose, , and
I.e.,
Can we verify that is a safety invariant for modified switch?
How do we prove it?

## Slide 13: Inductive Safety Proof
Given TS and a property , prove that all reachable states of TS satisfy
Base case: Show that all initial states satisfy
Inductive case: assume state satisfies , then show that if , then must also satisfy
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?

## Slide 14: Inductive Invariant
A property is an inductive invariant of a transition system TS if
  Every initial state satisfies
  If any state satisfies , and , then satisfies
By definition, if is an inductive invariant, then all reachable states of TS satisfy , and hence it is also an invariant

## Slide 15: Proving inductive invariants: I
Consider transition system TS given by
  :
  : if then (else remains unchanged)
Is an inductive invariant?
Base case: is zero, so is trivially satisfied

## Slide 16: Proving inductive invariants: I
Inductive case:
  Pick an arbitrary state (i.e., arbitrary value for state variable ), say
  Now assume satisfies , i.e.,
  Consider the transition, there are two cases: (Note: is an integer)
    If , then after the transition, and
    If , then (because guard is not true), which is .
  In either case, after the update
  So is an inductive invariant, and the proof is complete
  :
  : if then

## Slide 17: Proving inductive invariants: II
Consider transition system TS given by
  : ,
  : if then (else remain unchanged)
Is an inductive invariant?
Base case: Initial state is (), so is trivially satisfied

## Slide 18: Proving inductive invariants: II
Inductive case:
Pick an arbitrary state (i.e. arbitrary value for state variable ), say
Now assume satisfies , i.e.,
Consider the transition if then
What if )? Clearly, does not satisfy !
So is not an inductive invariant for TS, and the proof fails

## Slide 19: Proving inductive invariants: III
Consider transition system TS given by
  : ,
  : if then (else remain unchanged)
Is an inductive invariant?
Base case: Initial state is (), so is trivially satisfied

## Slide 20: Proving inductive invariants: III
Inductive case:
Pick an arbitrary state (i.e. arbitrary value for state variable ), say
Now assume satisfies , i.e. and
Consider the transition
  If then , else
  Now, if , and thus . Thus, is satisfied
  Else case is trivially satisfied because do not change value
In both cases, holds, so, is an inductive invariant!

## Slide 21: What’s an inductive invariant for this system?
1
1
(0,0)
Unsafe

## Slide 22: How do we prove safety invariants?
To establish that is an invariant of TS:
Find another property such that
  (i.e., every state satisfying must satisfy )
  is an inductive invariant
    Show initial states satisfy
    For arbitrary , and any s.t. , show
This is a sound and complete strategy for establishing safety invariants

## Slide 23: Soundness and Completeness of Safety with Inductive Invariants
Formal system:
  a set of axioms,
  a grammar for specifying well-formed formulas,
  a set of inference rules for deriving new true formulas from axioms
Sound:
  Starting from the axioms and using inference rules of the formal system,
  cannot arrive at a formula that is equivalent to false.
Complete: Complete with respect to a property if
  every formula having the property can be derived using the inference rules
Proof rule for proving safety for a transition system is sound and complete:
  Sound: If a (safe) inductive invariant exists, then the system is indeed safe
  Complete: If the system is safe, an inductive invariant must exist
    May still be hard/undecidable to find!

## Slide 24: Safety Proof for Switch
Let’s try the inductive invariant:
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?
Base case: trivially satisfies
Inductive hypothesis: assume that a state satisfies
Inductive step: prove that any s.t. satisfies
  Case I:
    = [trivial]
    = [satisfies second conjunct in ]
  Case II:
    if , this implies that , so satisfies
    otherwise, this again implies that satisfies
So is an inductive invariant
Further, (note that every state satisfying will satisfy )
So is an invariant of the TS!

## Slide 25
Automatic Verification

## Slide 26: Reachability
A state of a transition system is reachable if there is an execution starting in some initial state that ends in .
Algorithm to compute reachable states from a given set of initial states (just BFS):
Procedure ComputeReach(TS)
  , k:=1;
  While
  Temp :=
  ForEach
  If () Temp := Temp
  EndForEach
  Temp,
  EndWhile
  Return
  EndProcedure
  To get a proof of safety, do reachability computation, and if ComputeReach(TS) = , then the TS is safe

## Slide 27: Reachability to compute invariants
Given TS and a property , prove that all reachable states of TS satisfy
Recall ComputeReach(TS), it actually gives an inductive definition of reachable states
  All states specified by are reachable using 0 transitions
  If a state is reachable using transitions, and is a transition in , then is reachable using transitions
  Reachable = Reachable using transitions for some

## Slide 28: Reachability
For discrete-timed, finite-state systems :
  Reachable set of states can be exactly computed
  Could be expensive if the number of states is large (state-space explosion problem)
Use abstraction to compress reachable state space
    If counterexample not found in abstract state space no counterexample exists
    If counterexample found in abstract state space need to check if counterexample is real (and if not refine the state space)

## Slide 29: Reachability for general processes
Timed, Continuous (Linear & Nonlinear), Hybrid processes: reachable sets are harder to compute: undecidable in general
Various approaches have been researched over last 25 years (we will look at this later)

## Slide 30: Model checking & Automatic Verification
Coming up with invariants and proofs requires considerable human ingenuity!
Initial techniques for formal verification i.e. rigorously establishing program correctness were all largely manual
Model checking (invented around 1981-82) was the first approach at trying to automate the process of proving program correctness
Model checking inventors,
ACM 2007 Turing Award winners
(L to R)
E. Allen Emerson
Ed Clarke
Josef Sifakis

## Slide 31: What is model checking?
Checking if all behaviors of the system model are contained within the behaviors specified by a property specification
E.g. specifications:
  When adaptive cruise control is engaged, the speed of the car is between 20 and 60mph
  Always, if the drone detects an obstacle along its current flight path, it makes a call to the re-planning module within 1 second
  No two robots can be within 2 meters of each other
First algorithm for model checking used “Kripke Structures” as models (a kind of labeled transition system), and CTL for specifications

## Slide 32
Detour to Branching-Time Logics

## Slide 33: Computation Tree Logic
LTL was a linear-time logic where we reason about traces
CTL is a logic where we reason over the tree of executions generated by a program, also known as the computation tree
We care about CTL because:
  There are some properties that cannot be expressed in LTL, but can be expressed in CTL: From every system state, there is a system execution that takes it back to the initial state (also known as the reset property)
  To understand pCTL (Probabilistic CTL), it’s good if you understand CTL 
  Can express interesting properties for multi-agent systems

## Slide 34: Computation Tree
We saw computation trees when understanding semantics of asynchronous processes
Basically a tree that considers “all possibilities” in a reactive program
nat x := 0; bool y:= 0
A x := (x + 1) mod 2
B: even(x) y: = 1-y
Process
Finite State machine

## Slide 35: CTL Syntax
Syntax of CTL |  |  | 
 |  | ¦ | Prop. in , negation, conjunction
 |  | ¦ | Exists NeXt Step
 |  | ¦ | Exists a Future Step
 |  | ¦ | Exists an execution where Globally in all steps
 |  | ¦ | Exists an execution where in all steps Until in some step
 |  | ¦ | In All NeXt Steps
 |  | ¦ | In All possible future paths, there is a future step
 |  | ¦ | In All possible future paths, Globally in all steps
 |  | ¦ | In All possible future executions, in all steps Until in some step
Syntax of CTL |  |  | 
 |  | ¦ | 
 |  | ¦ | Exists NeXt Step
 |  | ¦ | Exists a Future Step
 |  | ¦ | Exists an execution where Globally in all steps
 |  | ¦ | Exists an execution where in all steps Until in some step
 |  | ¦ | In All NeXt Steps
 |  | ¦ | In All possible future paths, there is a future step
 |  | ¦ | In All possible future paths, Globally in all steps
 |  | ¦ | In All possible future executions, in all steps Until in some step

## Slide 36: CTL semantics
Path properties: properties of any given path or execution in the program
Quantification over runs: Checking if a property holds over all paths or over some path
Example CTL operator:
For All executions
Eventually/In Some Future step

## Slide 37: CTL Semantics through examples

## Slide 38: CTL semantics through examples
: Along all
Paths, There is some future step where holds
: Along some
path, there is some future step where holds

## Slide 39: CTL semantics through examples
: Across all
paths, and for every successor in the path, holds
: Along some
path, always holds

## Slide 40: CTL Operator fun

## Slide 41: CTL advantages and limitations
Checking if a given state machine (program) satisfies a CTL formula can be done quite efficiently (linear in the size of the machine and the property)
Native CTL cannot express fairness properties
  Extension Fair CTL can express fairness
CTL* is a logic that combines CTL and LTL: You can have formulas like
CTL: Less used than LTL, but an important logic in the history of temporal logic

## Slide 42: CTL model checking
Atomic proposition : Label each state that satisfies
: Label a state if any successor satisfies
: Label a state if all of its successors satisfy
: Label all states satisfying as
Until there is no change:
Add states with label if it has a successor labeled

## Slide 47
No more states with at least one successor green!
Check the states you have: if it contains the initial state, then the model satisfies

## Slide 48: CTL model checking
: Label all states satisfying as
Until there is no change:
Add states with label if all its successors are labeled
: Label all states satisfying as
Until there is no change:
Remove label from a state if it does not have any successor labeled

## Slide 50
Cannot remove any more states as all remaining states have at least one green successor!
Check the states you are left with: if it contains the initial state, then the model satisfies

## Slide 51
: What if bottom state was not green?

## Slide 52: : What if bottom state was not green?
Cannot remove any more states as all remaining states have at least one green successor!
Check the states you are left with: if it contains the initial state, then the model satisfies

## Slide 53: Greatest and least fixpoints
similar to
: similar to and (with the caveat that needs to be satisfied on every state that has a successor to a state marked
Fixpoint = point at which there is no change, i.e.
Consider the operation of adding/removing states as the function
  Fixpoint = Point at which you can no longer add/remove states
Least fixpoint = When adding states, smallest set you can get?
  You can always add all the states: not very useful
Greatest fixpoint = When removing states, largest set you can get?
  You can always remove all the states: not very useful

## Slide 54: CTL model checking in a nutshell
Algorithm based on Fixpoint computation
Many improvements to CTL model checking over the years (with the help of symbolic algorithms to accelerate fixpoint computation, represent sets of states, etc.)
Bounded model checking:
  Don’t check the entire state space using a “backward reachability” algorithm, but instead go forward in time from the initial state
  Use of SAT solvers to check feasibility of paths to failure states
Many good model checkers: NuSMV, CBMC, etc.

## Slide 55
LTL model checking

## Slide 56: LTL Model checking
Construct composition of the original transition system and the Büchi monitor
If there are cycles in the product automaton that visit the states specified by the Büchi condition, then we have found a violation
Reachable cycles in process composition correspond to counterexamples!
Implemented in many verification tools (e.g. the SPIN model checker developed at NASA JPL)
Many open-source tools to translate LTL properties to Büchi monitors: quite popular in the robotics domain [Spot, LTL2BA, …]

## Slide 57: LTL is a language for expressing system requirements
So far, we have seen how we can express behaviors of individual system traces using LTL
A system starting from some initial state satisfies an LTL requirement if all system behaviors starting in satisfy the requirement
Denoted as
E.g., a system is safe w.r.t. a safety requirement if all behaviors satisfy
Does (Blinker, (x0,y0)) (x0)?
nat x := 0; bool y:= 0
A x := x + 1
B: even(x)
y: = 1-y
Blinker

## Slide 58: Processes & Fairness
nat x := 0; bool y:= 0
A x := x + 1
B: even(x)
y: = 1-y
Blinker
Liveness property: (x 10)
  Is this property guaranteed to hold?
  No, task A may be executed less than 10 times.
Liveness Property: y (eventually y is 1)
  Is this property guaranteed to hold?
  No, task B may never be selected for execution!
But, this seems like a very unrealistic or broken scheduler!
For infinite executions involving multiple tasks, it is important for the execution to be fair to each task

## Slide 59: Weak vs. Strong fairness
A fairness assumption is a property that encodes the meaning of what it means for an infinite execution to be fair with respect to a task.
Weak fairness: If a task is persistently enabled, then it is repeatedly executed.
  I.e. if after some point the task guard is always true, then the task is infinitely often executed.
Strong fairness: If a task is repeatedly enabled, then it is repeatedly executed.
  I.e. if the task guard is infinitely often true, then the task is infinitely often executed.
nat x := 0; bool y:= 0
A x := x + 1
B: even(x)
y: = 1-y
Blinker

## Slide 60: Expressing fairness assumptions in LTL: I
Fairness assumptions can be expressed in LTL!
Add a new variable taken that takes value ‘A’, ‘B’
Weak fairness: ((taken = ))
Task A: is , so this simplifies to: wf(A) (taken=A)
Task B: wf(B) (even(x)) (taken=B)
Does (wf(A) wf(B)) (x 10)?
  Yes!
Does (wf(A) wf(B)) y?
  No!
nat x ; bool y
A x := x + 1; takenA
B: even(x)
y: = 1-y; taken B
Blinker
{A,B,} taken

## Slide 61: Expressing fairness assumptions in LTL: II
Strong fairness: ((taken = ))
Task A: is , so this simplifies to: sf(A) (taken=A)
Task B: sf(B) (even(x)) (taken=B)
Does (sf(A) sf(B)) (x 0)?
  Yes!
Does (sf(A) sf(B)) y?
  Yes!
nat x ; bool y
A x := x + 1; takenA
B: even(x)
y: = 1-y; taken B
Blinker
{A,B,} taken
Was verified: If a process satisfies a liveness requirement under weak fairness, it satisfies it under strong fairness, but converse is not true in general.

## Slide 62
Formal verification for Dynamical Systems

## Slide 63: Safety verification using barrier certificates
Barrier certificate: safety invariant for a continuous dynamical system
It establishes an invisible barrier that trajectories of a system cannot cross
  (think of it as a force-field)
Reasoning very similar to that of an inductive invariant
  Establish that the initial states all lie within the barrier
  Establish that the unsafe states are all outside the barrier
  Show that the next states for all states on the barrier are inside the barrier

## Slide 64: Strict barrier certificate
Given system
Function that serves as a classifier between good and bad states
Barrier conditions:
  (The last condition models the barrier pushing the system back!)
Unsafe
Initial

## Slide 65: Example
  Initial state set:
  Unsafe set:
Barrier:
  From plot:
    for initial states, ,
    for unsafe states,
Unsafe
Initial
Barrier

## Slide 66: Example
Finally, =
  =
    =
    =
From the plot, the above function is always negative for values of where
Barrier

## Slide 67: Time-bounded Reachability
Verification basics and Hybrid Systems lecture: reachability analysis using a “fix-point based algorithm”
  uses a breadth-first approach to compute reachable states over an infinite time-horizon
Barrier certificates: also provide infinite time safety results, but require manual ingenuity in coming up with a barrier; difficult to do for hybrid/nonlinear systems
Time-bounded reachability: Starting from some initial state in a given set of initial states, does the system behavior ever reach an unsafe state within a given time bound?

## Slide 68: Problem definition
Let be the solution trajectory of a given dynamical system (could be nonlinear, hybrid, timed, …) when the system starts in initial state
Time-bounded reachability: Prove that:
Counterexample to time-bounded reachability shown below
Unsafe
?
Trajectory segment with unsafe states
Trajectory segment with safe states

## Slide 69: Solutions to time-bounded reachability
To solve time-bounded reachability exactly:
  Compute set of all states reachable from :
  Check if is empty
  Challenge: computing is very hard (even for the simplest case of general linear dynamical systems)
Instead, we focus on approximating
  Under-approximation
  Over-approximation
  Combination of both

## Slide 70: Under-approximation
When we under-approximate the set of initial states, at each time, the set of reachable states that we compute is a subset of the actual set of reachable states
Best example of under-approximation is (guaranteed) numerical simulation
  Guaranteed numerical simulation: better than numerical integration schemes as it gives bounds on error in numerical integration (e.g. VNODE)
Under-approximation is:
  Sound for bug-finding: if we find a bug, then it is really a bug
  Unsound for verification: if we do not find a bug, does not mean the system is safe

## Slide 71: Under-approximation: sound for bug-finding
The good case: under-approximation found a trace that contained unsafe states – we found a bug in the system!

## Slide 72: Under-approximation: unsound for verification
The bad case: under-approximation did not find a trace that contained unsafe states – we cannot conclude anything.

## Slide 73: Over-approximation
When we over-approximate the set of initial states, at each time, the set of reachable states that we compute is a superset of the actual set of reachable states
Most formal verification techniques are based on over-approximation
Over-approximation is:
  Unsound for bug-finding: if we find a bug, then it may not really be a bug
    Because of over-approximation error
  Sound for verification: if we do not find a bug, we have a proof that the system cannot reach an unsafe state in any time in

## Slide 74: Reachability for piecewise affine (PWA) systems
PWA systems are a simplification of hybrid automata
For a PWA system with modes:
  Each mode described by an affine invariant of the form
  In each mode the dynamics are described as: +
A lot of research over last 20 years on computing the set of reachable states for PWA systems
  Focus: reduce approximation error and increase scalability (in number of modes)
  Tools: PHAver, d/dt, CheckMate, SpaceEx

## Slide 75: Reachability for affine systems
Recall that for a linear system (for now assume no inputs):
Let , now is just some constant matrix
If is some polyhedral set, we can compute the exact set of reachable states for every state in at time , because is just a linear transform
Thus, we get
Could be acceptable for continuous systems: between discrete time steps, solution remains in the neighborhood of the aproximations (and we can over-estimate this neighborhood numerically)

## Slide 76: Problem for CPS (hybrid systems)
Controller may be event-triggered, where it detects the level of a certain physical quantity, and based on that changes mode of operation
An event firing between consecutive time steps could take the PWA system in a different mode!
We need to account for what may happen between time-steps
This is done by covering the reach-sets computed at times and by a shape that includes both
Lots of research done on which shape is the best, and different shapes have different tradeoffs
  Ellipsoids, Zonotopes, Support Functions
  SpaceEx tool uses support functions, and is pretty accurate for reasonably sized PWA systems now
Wrong!

## Slide 77: Reachability for nonlinear systems
Not all systems can be modeled as PWA!
Nonlinear systems:
  Approach I: first PWA-ize the system, then do reachability. Drawback: Error encountered during PWA-ization accumulates
  Approach 2: use more interesting models such as Taylor models (based on Taylor series representations): used in tool Flow*
  Approach 3: solve the problem using a powerful nonlinear SMT solver: used in tool dReach

## Slide 78: Combining under and over-approximations
Also known as simulation-guided reachability analysis
Main idea:
  Sample some initial states, perform simulations starting from these states
  Use “continuity”-like arguments to bloat the trajectories in a sound manner
  If bloated trajectories cover initial state space, go to step 4, if not go back to step 1
  If bloated trajectories do not intersect unsafe set, conclude system is safe. If bloated trajectories intersect unsafe set, try to refine bloated trajectories to check if there is a true counterexample

## Slide 79: Simlulation-guided reachability depiction
Unsafe
Initial
Simulation Trace up to time T
Reach-Tube up to time T

## Slide 80: Secret sauce: how to bloat
Main idea: Solutions of ODEs are “sensitive” to their initial conditions
Such sensitivity gives an estimate on how far two trajectories can go if they start apart
A key notion is a discrepancy function that bounds how far trajectories can grow
Obtaining a that shows trajectories remain bounded within some reasonable factor of the distance between their initial conditions is very useful
  We only simulate from , and we know how all neighbors of will behave!
Technique implemented in tool C2E2, DryVR

## Slide 81
Probabilistic Verification

## Slide 82: PCTL
Syntax of PCTL |  | 
State formulas: |  | 
 |  | : nonempty interval ,
Path formulas: |  | 
Syntax of PCTL |  | 
State formulas: |  | 
Path formulas: |  | 
PCTL formulas are state formulas, path formulas used to define how to build a PCTL formula

## Slide 83: Example PCTL formulas
: probability of eventually reaching the goal is in
  Probability of possible outcomes for a fair die
  Probability of reaching a state from where you almost surely are safe within 5 steps where you do not run into an obstacle is greater than
Almost surely safe does not mean always safe!

## Slide 84: PCTL equivalences
Note that in PCTL, you cannot negate path formulas (syntax does not allow)!
But,
Here, is the negation of the comparison operator. E.g.,

## Slide 85: PCTL vs. CTL
can be thought of as a probabilistic analogue of CTL
However,

## Slide 86: Quantitative vs. Qualitative model checking
Quantitative model checking:
  Compute the probability bound of the outer operator which holds over given LTS
Qualitative model checking
  Check if under the given bound the formula is true
  Can be solved by qualitative model checking: compute the actual bound and then compare

## Slide 87: Model checking PCTL
Overall algorithm similar to model checking CTL
Given DTMC
= Probability of satisfying the path formula in the set of paths starting from

## Slide 88: Computing
Computing
For all , we need to compute
Let represent the state-indexed vector, where:
Then,

## Slide 89: Computing

## Slide 90: Computing
Note that this is a system of linear equations, where each is a variable
We can solve this using standard methods to compute the probability

## Slide 91: Types of problems in Probabilistic Verification
Qualitative Verification: Given Markov Chain and a PCTL formula where is some given constant, does ?
Quantitative Verification: Given Markov Chain and a PCTL formula where is unknown, find s.t. is true

## Slide 92: PCTL
0.2
1
Accelerate
Constant Speed
Idling
Brake
0.2
0.5
0.3
0.8
0.05
0.05
0.5
0.4
0.5
0.4
0
0.1
Qualitative: Does this formula hold in state Brake?
Yes
Quantitative: Value of ?
Compute for all , pick smallest
  = 0.5 + 0.2 + 0.3*0.5 + 0.3*0.2
  = 0.91
I.e. with probability 0.91, driver checks cell phone within 2 steps
0
0
: Checking cellphone
: Feeling sleepy

## Slide 93: PCTL vs. CTL
can be thought of as a probabilistic analogue of CTL
However,

## Slide 94: Probabilistic vs. Nondeterministic verification
Toss a coin repeatedly until “tails” is thrown
Is “tails” eventually thrown along all paths?
  CTL: tails
  Result: false
  Why?
Is the probability of eventually thrown “tails” equal to 1?
  PCTL:
  Result: true
  Probability of path is zero!
0.5
0.5
1
1

## Slide 95: Geometric distribution for discrete random variables
Given and , the prob. mass function of a geometric distribution is:

## Slide 96: Residence/Dwell times
Residence time in a state of a Markov chain is an r.v. with geometric distribution
  …
What is the expected time you stay in a state?
What is the variance?

## Slide 97: Continuous Time Markov Chains
Time in DTMC is discrete
CTMCs:
  dense model of time
  transitions can occur at any time
Two ways of modeling CTMCs:
  dwell time in a state is (negative) exponentially distributed
  transition rate is (negative) exponentially distributed

## Slide 98: Exponential distribution
Continuous random variable : probability density function
A negative exponentially distributed random variable X with rate , has probability density function (pdf) defined as follows:

## Slide 99: Exponential distribution properties
Cumulative distribution function (CDF) of is then:
  I.e,. zero probability of doing transition out of a state in duration , but probability becomes as
Fun exercise: show that above CDF is memoryless, i.e.,
Fun exercise 2: If and are r.v.s negatively exponentially distributed with rates and , then
Fun exercise 3: If are negative exponentially distributed with rates

## Slide 100: CTMC modeled with n.exp. distributed dwell time
Tuple
  is a finite set of states
  is a transition probability function
  is the init. dist.
  is a set of Boolean propositions, and is a function that assigns some subset of Boolean propositions to each state
  is the exit-rate function
Dwell time in state negative exponentially distributed with rate
  Average residence time in state
  Bigger the exit-rate, shorter the average residence time
0.6
0.8
0.4
0.3
0.6
0.2
0.1
0.1
0.5
5

## Slide 101: CTMC modeled with n.e. distributed transition rate
Transition modeled as a r.v. that is negative exponentially distributed with rate
Bigger values of means lower probability of going from to
Probability of reaching state from :
Transition rate
Probability of moving from to in time :
Rate of exiting
Probability of going to

## Slide 102: CTMC example
Probability to go from state to is:
What is the probability of changing to some lane from in seconds?
0.6
0.8
0.4
0.3
0.6
0.2
0.1
0.1
0.5
5

## Slide 103: CTMC + PCTL
Recall that
Also recall that
Probability to go from to is:
?
  enabled in is
0.5
0.3
0.2

## Slide 104: Bibliography
Breach : https://link.springer.com/chapter/10.1007/978-3-642-14295-6_17
Prajna, S., & Jadbabaie, A. (2004, March). Safety verification of hybrid systems using barrier certificates. In International Workshop on Hybrid Systems: Computation and Control (pp. 477-492).
Duggirala, Parasara Sridhar, et al. "C2E2: a verification tool for stateflow models." International Conference on Tools and Algorithms for the Construction and Analysis of Systems.
Frehse, Goran, Colas Le Guernic, Alexandre Donzé, Scott Cotton, Rajarshi Ray, Olivier Lebeltel, Rodolfo Ripado, Antoine Girard, Thao Dang, and Oded Maler. "SpaceEx: Scalable verification of hybrid systems." In International Conference on Computer Aided Verification, pp. 379-395. Springer, Berlin, Heidelberg, 2011.
Chen, Xin, Erika Ábrahám, and Sriram Sankaranarayanan. "Flow*: An analyzer for non-linear hybrid systems." In International Conference on Computer Aided Verification, pp. 258-263. Springer, Berlin, Heidelberg, 2013.
Frehse, Goran. "PHAVer: Algorithmic verification of hybrid systems past HyTech." International workshop on hybrid systems: computation and control. Springer, Berlin, Heidelberg, 2005
Asarin, E., Dang, T., & Maler, O. (2002, July). The d/dt tool for verification of hybrid systems. In International Conference on Computer Aided Verification (pp. 365-370). Springer, Berlin, Heidelberg.
Fan, Chuchu, Bolun Qi, Sayan Mitra, Mahesh Viswanathan, and Parasara Sridhar Duggirala. "Automatic reachability analysis for nonlinear hybrid models with C2E2." In International Conference on Computer Aided Verification, pp. 531-538. Springer, Cham, 2016.
Donzé, Alexandre, and Oded Maler. "Systematic simulation using sensitivity analysis." In International Workshop on Hybrid Systems: Computation and Control, pp. 174-189. Springer, Berlin, Heidelberg, 2007