## Slide 1: Autonomous Cyber-Physical Systems: Planning and Decision-Making
Fall 2023. CS 513.
Instructor: Jyo Deshmukh

## Slide 2: Autonomous systems architecture
Sensing
Perception
Decision
Control
Actuation
Operating System/Hypervisor

## Slide 3: Sensing
Primary purpose is to know everything about the environment
Most of the software modules in the sensing modules deal with:
  Sensor fusion: (using KFs, EKFs, UKFs, etc.)
  Data preprocessing: e.g. converting LiDAR data into point-cloud representation, sampling video signals, compressing data
GPS
LiDAR
IMU
Radar
Camera

## Slide 4: Perception
Many things fall under the vague category of perception, list to the left is not complete
Localization:
  Strongly connected to sensor fusion
  May use algorithms such as particle filters in addition to Kalman filter
  Could further sub-divide into road-level localization in a map, or lane-level localization on a road, or localizing within a lane
Localization
Object Tracking
Object Detection
Traffic recognition
Road topology identification

## Slide 5: Perception
Object detection
  Use vision or deep learning algorithms to detect various kinds of objects
  Pedestrians, Bicyclists, other vehicles, traffic signs, lane markings, obstacles
  Objects could be static or dynamic, and detection algorithms may vary accordingly
Object tracking
  Tracking trajectories of moving objects
  Could be based on deep learning or algorithms like optical flow
Localization
Object Tracking
Object Detection
Traffic recognition
Road topology identification

## Slide 6: Decision
Prediction: Generate most probable trajectories of vehicles, pedestrians, obstacles in the environment
Mission/Route planning: Generate very high-level route plan based on way-points, maps
Reference planning: Generate trajectories for vehicle + Behavioral planning (traffic-aware): modify according to environment models
Motion planning: Synthesizing inputs for low-level actuators to match a higher-level plan
Obstacle avoidance: Stopping or maneuvering around an obstacle
Prediction
Behavioral Planning
Mission planning
Obstacle avoidance
Motion Planning

## Slide 7: Decision
Decision layer is the most software-intensive layer
Several algorithms have been proposed in the robotics and automotive community based on optimization, search-based planning, discrete decision-making (with state machines).
Current trend is to investigate application of AI/control techniques such as reinforcement learning/deep reinforcement learning
Prediction
Behavioral Planning
Mission planning
Obstacle avoidance
Motion Planning

## Slide 8: Control (Low-level control)
These algorithms have been typically deployed to cars before self-driving cars took off
Also, researchers are interested in knowing if existing algorithms can be made more efficient with data (models of the environment)
Drive-by-wire controlled by AI software
Techniques like model-predictive control are gathering momentum
Steering Control
Lateral stability control
Torque control
Energy management
Emissions control

## Slide 9: Planning is often hierarchical
Route Planning
Behavioral Planning
Lane following
Lane changing
Adaptive cruising
Intersection negotiation
Collision avoidance
Trajectory planning/Motion planning
Low-level Feedback control
Road topology, network
Perception layer outputs
Estimated pose and free space
Vehicle state estimates
User-specified
destination
Sequence of way-points
Motion specification
Reference path
Steering and throttle commands

## Slide 10: Route planning
Represent road network/topology as a directed graph
  Nodes represent way-points
  Edges represent a cost of traveling between nodes
Cost can represent time, distance, fuel economy, a weighted combination of some of these, etc.
Simplest solutions based on Dijkstra’s shortest-path or A* search algorithms
  In practice, these do not scale well
  Lots of different algorithms proposed in the literature5

## Slide 11: Dijkstra’s Shortest path algorithm
ShortestPath (Graph G(V, E), src)
  ; ;
A
C
D
E
F
B
3
2
6
6
5
5
1
5
 | A |  | B |  | C |  | D |  | E |  | F |  | Q
1 |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  | 3 | A | 6 | A | 6 | A |  |  | 
3 |  |  |  |  | 3 | A | 6 | A | 5 | C | 8 | C | 
4 |  |  | 10 | E | 3 | A | 6 | A | 5 | C | 8 | C | 
5 |  |  | 10 | E | 3 | A | 6 | A | 5 | C | 8 | C | 
6 |  |  | 9 | F | 3 | A | 6 | A | 5 | C | 8 | C | 
7 |  |  | 9 | F | 3 | A | 6 | A | 5 | C | 8 | C | 
 | A |  | B |  | C |  | D |  | E |  | F |  | Q
1 |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  | 3 | A | 6 | A | 6 | A |  |  | 
3 |  |  |  |  | 3 | A | 6 | A | 5 | C | 8 | C | 
4 |  |  | 10 | E | 3 | A | 6 | A | 5 | C | 8 | C | 
5 |  |  | 10 | E | 3 | A | 6 | A | 5 | C | 8 | C | 
6 |  |  | 9 | F | 3 | A | 6 | A | 5 | C | 8 | C | 
7 |  |  | 9 | F | 3 | A | 6 | A | 5 | C | 8 | C | 

## Slide 12: Dijkstra’s shortest path algorithm
Computes for each node, the shortest path from the source to that node
Classic example of a dynamic programming algorithm
Original algorithm runs in
Optimization using Fibonnaci Heaps allows complexity
Does not work for graphs with cycles or negative weights!
  Bellman-Ford algorithm for graphs with negative weights and cycles (but no negative cycles)
  Floyd-Warshall for finding shortest paths between all pairs of nodes

## Slide 13: Behavior planning
Plans high-level driving actions, driving maneuvers
Behavior planner considers static, dynamic obstacles +
  Driving: traffic rules, corner cases (emergency vehicles, construction)
  Flying: flight plan, corridors, no-fly zones
Examples:
  Driving:
    Cruise control, Adaptive Cruise Control
    Lane switching, merging
    Obstacle avoidance, Traffic lights
  Flying: Take-off, Landing, Hovering, Complex maneuvers

## Slide 14: Behavior planner
Inputs:
  Map: HD road map, road network, 3D map including no-fly zones
  Localization information (where am I?): using variety of sensors + using localization algorithms
  Perception of environment around the vehicle (using sensors)
Output:
  sequence of discrete actions/maneuvers based on own behaviors and behaviors of other actors in the environment

## Slide 15: Behavior Planning often uses trajectory prediction
Cars, cyclists: many models available
  Current “winners” based on deep/recurrent neural networks
Human motion prediction: much harder, lots of ongoing research

## Slide 16: Physics-based trajectory prediction
Evolution models: dynamic or kinematic
  Dynamic models:
    Use Lagrangian mechanics models (sum of all forces on the vehicle should be zero)
    Usually simplified to be fast enough for trajectory prediction (e.g. 2-wheeled bicycle model)
  Kinematic models:
    Ignore many forces, focus on velocity, direction of vehicle etc.
    E.g. constant velocity, constant acceleration, constant turn rate and velocity, constant turn rate and acceleration models

## Slide 17: Trajectory prediction
Use kinematic or dynamic model and “evolve” it in time:
  usually not reliable because it assumes perfect knowledge of current state
Simulate based on evolution model but add Gaussian noise
Explicitly model uncertainty parameters and do Monte Carlo simulation
(1)
(2)
(3)
Pictures from: https://robomechjournal.springeropen.com/articles/10.1186/s40648-014-0001-z

## Slide 18: Collision prediction
Check if ego trajectory will intersect with predicted trajectory (discretize at each time step, or compute analytically)
Risk indicators for collision
  Time to collision (TTC): time remaining before collision may occur
    used to decide when to apply brakes, to identify which is the least dangerous maneuver
  Time to react: Time available for driver to act before collision is inevitable
    Used to identify latest time at which braking/acceleration/steering etc. can help avoid collision

## Slide 19: Trajectory prediction for pedestrians
Physics-based : Dynamical models of pedestrians
  Single dynamic model or multiple dynamical models
Pattern-based: Learn motion patterns from data
  Sequential methods: Learn conditional models and recursively apply learned transition functions for inference
  Non-sequential methods: Model distribution over full trajectories
Planning-based methods (based on estimating pedestrian’s long-term goals)
Pattern-based methods using recurrent neural networks such as LSTMs are increasingly popular today

## Slide 20: Behavior planning: FSM-based planning
Each state in the FSM is a maneuver or “mode”
Decelerate
Track Speed
Distance to stop sign
threshold?
Distance to stop sign
threshold?

## Slide 21: Planning using finite state machines
States = finite set of driving contexts and behaviors, FSMs to represent possible transitions between contexts
Planning then becomes a problem of choosing appropriate transitions that ensure a desired behavior
Can view this is a 2-player game between the car’s controller (player 1) and the environment (player 2)
Game-theoretic approaches for FSMs can identify winning strategies for the controller

## Slide 22: Behavioral planning under uncertainty
FSM-based view may not adequately address uncertainty
Uncertainty exists in the intention of traffic participants
Intent prediction of cars, bicycles, pedestrians
  Techniques based on Gaussian mixture models
  Switching linear dynamical and stochastic systems
  Gaussian Process Regression
Big recent push: probabilistic planning formalisms using Markov Decision Processes such as Partially Observable Markov Decision Processes: RL/DRL

## Slide 23: Motion planning
Behavior plan decides a high-level set of maneuvers (e.g. cruise-in-lane, turn right, turn left, hover, etc.)
This plan needs to be translated into a reference path or a reference trajectory to be followed by the vehicle.
Motion planning computes a feasible reference plan that respects feasibility (according to vehicle dynamics), obstacle avoidance, while optimizing certain costs (e.g. maximizing comfort, minimizing battery usage, etc.)
Popular approaches
  Variational methods from nonlinear optimal control
  Graph-search approaches using discretization of the state-space
  Incremental tree-based methods

## Slide 24: Path planning vs. Trajectory planning
Path planning:
  Simply provides a parametric function
    is the configuration space or state-space of the vehicle
    gives the initial configuration, and gives the final configuration, and for all intermediate , gives the intermediate configurations
  May not include a velocity profile or those for other states, but delegates this to lower-level control
Trajectory planning: Is aware of vehicle dynamics and can account for dynamic obstacles

## Slide 25: Trajectory planning
Defines a parametric function , where
  is the planning horizon, and is the set of configurations
  precisely describes how the vehicle’s behavior evolves in configuration space at each time
Trajectory planning is a more nuanced version of path planning

## Slide 26: Trajectory planning setup
: set of all continuous functions from to
Let , then:
  (where is a set of initial configurations/states)
  (where is a set of goal states)
Set of all allowed states at time denoted as
encodes holonomic constraints
  A constraint is holonomic if you can express it as , where the ’s are coordinates, i.e., constraint depends only on spatial configuration
  Holonomic constraints can encode path constraints, and dynamic and static obstacles

## Slide 27: Trajectory planning setup continued
is a differential constraint specifying constraints on smoothness of the path, velocity, acceleration, jerk constraints etc.
is a cost functional mapping any trajectory to some cost in
Optimal trajectory can be stated as follows:

## Slide 28: Trajectory planning setup continued
Trajectory planning in dynamic environments and static path planning are both PSPACE-hard problems
  At least as complex as checking SAT of a quantified Boolean formula (QBF)
  Example QBF formula:

## Slide 29: Variational methods
Rely on results from nonlinear continuous optimization
We transform the trajectory optimization to the following standard form:
Standard trick to go from constrained to unconstrained optimization is to introduce penalty functions
  Penalty method:
  Barrier function method:
  ()

## Slide 30: Graph-search-methods
Variational methods may get stuck in local optima, graph-search methods try to do global search
Configuration space is represented as a graph , where is a set of selected discrete configurations, and is a set of edges, where each edge is labeled by the path segment that the edge represents.
  If , then and
Feasible path can be found by concatenating feasible edges
Does require discretization of the configuration/state space!
  Hand-crafted lane graphs2
  Geometric representations
  Sampling-based discretization

## Slide 31: Sampling-based methods: Roadmaps
Typical constraints (differential, holonomic) are usually very difficult to obtain at real-time through sensors
Sampling-based methods explore reachability of free configuration space by trying to apply controls (steering) and checking for collisions
Main purpose of these methods is to construct a roadmap, and use it for planning
Steering functions:
  Random : returns a path obtained by applying a random steering command
  Heuristic: tries to guide vehicle from point to point
  Exact: computes exact path that takes vehicle from to
  Optimal: Returns an optimal exact path

## Slide 32: Probabilistic Roadmap (PRM) Construction
for
  for
    if
    endif
  end
End
return
:
Return points on a grid
Random samples
:
-nearest neighbors using appropriate distance function
Points within a ball of radius around
Trajectory plan: Use Dijkstra’s shortest-path algorithm on the resulting roadmap

## Slide 33: Heuristic search A*
Once we have a roadmap, how do we find the best path in the roadmap?
Dijkstra’s shortest path algorithm uses best first search to build a tree representing shortest paths from a given source to all other vertices in the graph
We typically need a path to only a single vertex (in the goal set), in this case a heuristic can be used to guide the search process
Most prominent heuristic search algorithm is A*
Shown to be optimally efficient if heuristic function is admissible (never overestimates the cost)

## Slide 34: How A* works
Constructs tree of paths from initial node, expanding paths one step at a time, till one of the path reaches the goal
In each iteration, A* determines which partial path to expand based on an estimate of the cost
It selects the path that minimizes , where .
= cost of path from start node to ,
= estimate of the cheapest cost to go from to the goal
: heuristic function
is admissible, if it never over-estimates actual cost to get to the goal
Dijkstra’s shortest path: special case of A*, where

## Slide 35: A* implementation
A* (Graph G(V, E), )
  /* newly discovered nodes, not yet explored */
  /* already evaluated nodes */
  /* best predecessor node so far */
  /* cost of reaching from */
    /* estimate of reaching from via */
  ;
  ;
  /* if you are here, it means is either a new open node or has we just found a lower cost path to */

## Slide 36: A* example
 | 0 | 1 | 2
0 | Start |  | Goal
1 |  |  | 
2 |  |  | 
3 |  |  | 
  ;
  ;

## Slide 37: A* example
 | 0 | 1 | 2
0 | Start |  | Goal
1 |  |  | 
2 |  |  | 
3 |  |  | 
  ;
  ;

## Slide 38: A* example
 | 0 | 1 | 2
0 | Start |  | Goal
1 |  |  | 
2 |  |  | 
3 |  |  | 
  ;
  ;

## Slide 39: A* example
 | 0 | 1 | 2
0 | Start |  | Goal
1 |  |  | 
2 |  |  | 
3 |  |  | 
  ;
  ;

## Slide 40: Weighted A*
Admissibility criterion forces A* to inspect all equally promising paths to find the optimal
Approximate shortest paths can be found by relaxing the admissibility criterion (i.e. the function)
  This guarantees that the path found is no worse than times the optimal path
Weighted A* variants involve defining a heuristic that is a function of . E.g. static weighted A* uses

## Slide 41: Many variants of A*
Real-time re-planning: D*, Focused D*, D* Lite: recompute shortest path anytime the underlying graph changes, making use of results from previous search
Anytime search algorithms: Quickly find a (possibly sub-optimal) path first, and continue to improve the solution if there is more computational time
  Anytime A*: weighted heuristic that continues searching using cost of previously identified path as upper bound and admissible heuristic as lower bound
  Other variants such as Anytime Repairing A*, Anytime Dynamic A* etc.

## Slide 42: Rapidly Exploring Random Trees (RRTs)
RRT one of a family of algorithms based on incremental sampling, i.e. when you do not want to a priori build the entire roadmap
Also known as single-query PRMs
Very fast algorithm, allows on-the-fly construction of paths
// is a tree
for
// Find point in that is closest to
// Find control that gets you closest to from
end
Plan = Path from to s.t.

## Slide 43: RRT in action
Target
Sample goal
Select closest neighbor
Find collision-free control
Obstacle
Target
Obstacle
Target
Obstacle

## Slide 44: Problems with RRT
Suppose you are given a function that assigns costs to paths
RRT solution is usually far from optimal
Karaman & Frazzoli (2010) showed that probability of RRT converging to an optimal solution is 0
First alternative: RRG (Rapidly exploring Random Graph)
  Connects new sample to all vertices within some distance to it
  Can create graphs with cycles
  Improves optimality: probability of RRG converging to an optimal solution is 1

## Slide 45: Many variants of PRMs and RRTs
Many variants: RRT* (rewires the tree as better paths are found), PRM*, etc.
Some of them add optimality criteria such as costs on edges
Algorithms differ in the underlying structure maintained: PRM (forest), RRT (tree), RRG (graphs with possible cycles), RRT* (acyclic graphs) etc.
There are two key considerations:
  Probabilistic completeness: given infinite time, will the procedure identify a path to the goal set
  Asymptotic optimality: does the optimal path found by the algorithm converge to the actual optimum in the limit

## Slide 46: Combining RRTs with STL
Define path planning objectives in STL
Define robustness of STL on partial trajectories
Use RRT to explore the search space
When selecting nearest neighbors of the goal point, select ones with high robustness
Allows path-planning with STL objectives!
Combining RRTs with LTL objectives has been extensively studied in the literature

## Slide 47: Bibliography
Pendleton, Scott Drew, Hans Andersen, Xinxin Du, Xiaotong Shen, Malika Meghjani, You Hong Eng, Daniela Rus, and Marcelo H. Ang. "Perception, planning, control, and coordination for autonomous vehicles." Machines 5, no. 1 (2017): 6.
Paden, Brian, et al. "A survey of motion planning and control techniques for self-driving urban vehicles." IEEE Transactions on Intelligent Vehicles 1.1 (2016): 33-55. https://arxiv.org/pdf/1604.07446.pdf
Katrakazas, C., Quddus, M., Chen, W. H., & Deka, L. (2015). Real-time motion planning methods for autonomous on-road driving: State-of-the-art and future research directions. Transportation Research Part C: Emerging Technologies, 60, 416-442.
https://en.wikipedia.org/wiki/A*_search_algorithm
Bast, D. Delling, A. Goldberg, M. Müller-Hannemann, T. Pajor, P. Sanders, D. Wagner, and R. F. Werneck, “Route planning in transportation networks”, https://arxiv.org/pdf/1504.05140.pdf
https://www.annualreviews.org/doi/pdf/10.1146/annurev-control-060117-105157
https://journals.sagepub.com/doi/pdf/10.1177/0278364920917446?casa_token=rawjqqG8ZdQAAAAA:xPgWGamXwyciEb8pAqHcaHYXF96Mz7cmu4TKtvk7jMxz8X63ndFuxm5X7osUQRaibeC2aN_g2WCw1Q