## Slide 1: Autonomous Cyber-Physical Systems: Signal Temporal Logic
Spring 2018. CS 599.
Instructor: Jyo Deshmukh

## Slide 2: Overview
Last lecture
  CTL, pCTL
This lecture
  STL: A requirements language for Cyber-Physical Systems

## Slide 3
Let’s reduce the engine size and add a turbocharger
Sure, how does the turbocharger behave? How can I model it?
It’s still being designed
Let me assume a textbook model..
Here’s some hardware spec data
I enhanced the physics-based model and tuned it to match your data, and have a controller that works!
Actually, here’s some new data, the hardware specs changed
Here’s my final hardware design
Here’s my final controller specification model
The new specs need to have X,Y,Z characteristics
How does CPS software design actually happen in reality?
Closed-Loop System Model

## Slide 4: What are closed-loop models used for?
Testing design quality!
Check transient response of x when driving with highway 73 pattern with temperature below freezing
Chief Engineer
Control Designer

## Slide 5: Typical day in a control designer’s life
Uh Oh!
time
,
time
… should be okay
,
Looks good
time
,

## Slide 6: Signal Temporal Logic (STL)
STL can be used as a logic to formalize many control-theoretic properties, properties of path-planning algorithms, express timing constraints and causality relations
LTL/CTL: languages to express properties of discrete-timed, discrete-valued reactive systems
  Operating systems, Distributed systems, shared-memory programs, device drivers etc.
STL: started as a logic to express properties of mixed-signal and analog circuits
Invented by Dejan Nickovic and Oded Maler from Verimag

## Slide 7: Before STL, there was MTL
MTL = Metric Temporal Logic
Extended LTL with the notion of temporal operators that range over time-intervals
Example formula:
  : At all times between time 0 and 3, the propositions and are true
MTL required separate definition of predicates. E.g. could mean “it is raining”, or it could mean “, etc.
STL introduced signal predicates as atomic formulas

## Slide 8: Expressing specifications in STL
0
100
50
1
3
Always between time 0 and 100
Eventually at some time t between time 20 and 60
From that time t, always till the end of the signal trace
0
100
1
-0.1
+0.1
60

## Slide 9: Can we express our engineer’s requirements?
Uh Oh!
time
,
time
… should be okay
,
Looks good
time
,

## Slide 10: STL is interpreted over Signals
Signal is a function from a time domain to a value domain
Time domain can be
  A discrete domain: e.g. positive integers (traces for LTL), arbitrary finite set of values,
  A dense domain: e.g. a continuous set of real-valued time-instants
Value domain can be
  A finite domain: e.g. Booleans (traces for LTL), some finite enumeration (e.g. a set of modes)
  An infinite domain: e.g. integers, reals, etc.
  A combination of any number of these

## Slide 11: More about Signals
A signal that has only one kind of value domain is called univariate (only one thing varies), and with multiple domains is called multivariate
Number of distinct components of a signal is called its dimension
Thus, signal value at any given time is a vector of values, each of which may come from a different value domain
If we designate a time domain by , and a value domain by , then signals are basically functions from to
In this lecture, we will assume that the time domain is the dense domain , and the value domain is , where is the signal dimension
Thus a signal is a function from to

## Slide 12: STL Syntax
Syntax of STL |  |  | 
 |  | ¦ | is a function over the signal ,
 |  | ¦ | Negation
 |  | ¦ | Conjunction
 |  | ¦ | At some Future step in the interval
 |  | ¦ | Globally in all times in the interval
 |  | ¦ | In all steps Until in interval
Syntax of STL |  |  | 
 |  | ¦ | 
 |  | ¦ | Negation
 |  | ¦ | Conjunction
 |  | ¦ | 
 |  | ¦ | 
 |  | ¦ | 

## Slide 13: STL semantics
Semantics of STL specified recursively over a signal at each time
For each STL formula , here’s how we define it’s semantics:
If is the signal predicate , then iff
,

## Slide 14: Recursive Boolean Semantics of STL
 | ,

## Slide 15: Recursive Boolean Semantics of STL
0.1
0.2
0.3
0.4
0.5
0.6
0.7
1
2
3
 | T | T | T | F | F | T | T | T
 | T | T | T | F | F | T | T | T
0,0
T
at time | 
at time | Minimum over robustness of for
at time t | Maximum over robustness of for
T
T
T
T
T
T

## Slide 16: Example STL formulas: Overshoot
time
Overshoot:
Step:

## Slide 17: Example STL formulas: Settling Time
time
Settling Time:
Step:

## Slide 18: Robot Path Specification
Whenever the robot visits the kitchen, it should visit the bedroom within the next 15 mins.
Robot should not go to the bathroom in the first 60 mins.
: Box describing room
: Position of robot at time
Kitchen
Bedroom
Living Room
Bathroom
Study
TV
Passage
(0,5)
(15,25)

## Slide 19: Robot Path Specification
Kitchen
Bedroom
Living Room
Bathroom
Study
Passage
The robot battery should last between 4 hours and 6 hours
For the first 10 hours, the robot is never in any room for more than mins

## Slide 20: STL has quantitative semantics
Quantitative semantics defined using the notion of a Robust Satisfaction Value, or Robustness Value
Robustness is a function that maps
  a given trace ,
  a formula ,
  and a time
  to some real value
We can interpret robustness as “distance to violation” of a given formula

## Slide 21: Distance to violation/satisfaction
GOOD
GOOD
How far is
bad?
0
100
50
3
BAD
0
100
50
3
BAD
How bad is the violation?

## Slide 22: How do quantitative semantics help our engineer?
Uh Oh!
time
,
time
… should be okay
,
Looks good
time
,
= -0.2
= 0.01
= 0.2

## Slide 23: Recursive Quantitative Semantics
, | 

## Slide 24: Robustness computation example
0.1
0.2
0.3
0.4
0.5
0.6
0.7
1
2
3
 | 1 | 1 | 0.5 | -0.5 | -1 | 0.5 | 0 | 0.5
 | 1 | 1 | 0.5 | -0.5 | -1 | 0.5 | 0 | 0.5
0,0
1
1
0.5
0.5
0.5
0.5
at time | 
at time | Minimum over robustness of for
at time t | Maximum over robustness of for
0.5

## Slide 25: Next lecture
How do we use STL for testing, falsification
How can we infer STL requirements from a model

## Slide 26: Bibliography
G. Fainekos, and G. J. Pappas. Robustness of temporal logic specifications for continuous-time signals. Theoretical Computer Science 2009.
Maler, Oded, and Dejan Nickovic. "Monitoring temporal properties of continuous signals." Formal Techniques, Modelling and Analysis of Timed and Fault-Tolerant Systems. Springer, Berlin, Heidelberg, 2004. 152-166.
Donzé, Alexandre, and Oded Maler. "Robust satisfaction of temporal logic over real-valued signals." International Conference on Formal Modeling and Analysis of Timed Systems. Springer, Berlin, Heidelberg, 2010.
Kapinski, James, et al. ST-Lib: A library for specifying and classifying model behaviors. No. 2016-01-0621. SAE Technical Paper, 2016.