## Slide 1: Autonomous Cyber-Physical Systems: Autonomous Systems Software Stack
Spring 2018. CS 599.
Instructor: Jyo Deshmukh

## Slide 2: Overview
Start of Module 3!
  Software Modules in an Autonomous System Software Stack
  Algorithms
This lecture
  Basic introduction to some popular architectures and approaches

## Slide 3: Autonomous systems software architecture
Software architecture describes key software components and their inter-relationships.
A very general software architecture will give you insight about all the software that goes into making the autonomous system; this will include:
  A single real-time operating system or a hypervisor that controls several operating systems
  Libraries and components for interfacing with specialized components like GPUs/NPUs, memory, I/O etc.
  Application-layer software (the interesting part that makes the autonomous system, autonomous)
We will focus only on the application layer software architecture

## Slide 4: Self-driving car architecture
Sensing
Perception
Decision
Control
Actuation
Operating System/Hypervisor

## Slide 5: Sensing
Primary purpose is to know everything about the environment
Most of the software modules in the sensing modules deal with:
  Sensor fusion: (using KFs, EKFs, UKFs, etc.)
  Data preprocessing: e.g. converting LiDAR data into point-cloud representation, sampling video signals, compressing data
GPS
LiDAR
IMU
Radar
Camera

## Slide 6: Perception
Many things fall under the vague category of perception, list to the left is not complete
Localization:
  Strongly connected to sensor fusion
  May use algorithms such as particle filters in addition to Kalman filter
  Could further sub-divide into road-level localization in a map, or lane-level localization on a road, or localizing within a lane
Localization
Object Tracking
Object Detection
Traffic recognition
Road topology identification

## Slide 7: Perception
Object detection
  Use vision or deep learning algorithms to detect various kinds of objects
  Pedestrians, Bicyclists, other vehicles, traffic signs, lane markings, obstacles
  Objects could be static or dynamic, and detection algorithms may vary accordingly
Object tracking
  Tracking trajectories of moving objects
  Could be based on deep learning or algorithms like optical flow
Localization
Object Tracking
Object Detection
Traffic recognition
Road topology identification

## Slide 8: Decision
Prediction: Generate most probable trajectories of vehicles, pedestrians, obstacles in the environment
Mission/Route planning: Generate very high-level route plan based on way-points, maps
Reference planning: Generate trajectories for vehicle + Behavioral planning (traffic-aware): modify according to environment models
Motion planning: Synthesizing inputs for low-level actuators to match a higher-level plan
Obstacle avoidance: Stopping or maneuvering around an obstacle
Prediction
Behavioral Planning
Mission planning
Obstacle avoidance
Motion Planning

## Slide 9: Decision
Decision layer is the most software-intensive layer
Several algorithms have been proposed in the robotics and automotive community based on optimization, search-based planning, discrete decision-making (with state machines).
Current trend is to investigate application of AI/control techniques such as reinforcement learning/deep reinforcement learning
Prediction
Behavioral Planning
Mission planning
Obstacle avoidance
Motion Planning

## Slide 10: Control (Low-level control)
These algorithms have been typically deployed to cars before self-driving cars took off
Recent trend is to “drive-by-wire”, i.e. replace mechanical and hydraulic components by electrical and electronic components
Also, researchers are interested in knowing if existing algorithms can be made more efficient with data (models of the environment)
Techniques like model-predictive control are gathering momentum
Steering Control
Lateral stability control
Torque control
Energy management
Emissions control

## Slide 11: Bibliography
Shaoshan Liu, Jie Tang, Zhe Zhang, and Jean-Luc Gaudiot, CAAD: Computer Architecture for Autonomous Driving, https://arxiv.org/ftp/arxiv/papers/1702/1702.01894.pdf
Thrun, Sebastian. "Toward robotic cars." Communications of the ACM 53, no. 4 (2010): 99-106.
Taş, Ö.Ş., Kuhnt, F., Zöllner, J.M. and Stiller, C., 2016, June. Functional system architectures towards fully automated driving. In Intelligent Vehicles Symposium (IV), 2016 IEEE (pp. 304-309). IEEE.
Ulbrich, S., Reschka, A., Rieken, J., Ernst, S., Bagschik, G., Dierkes, F., ... & Maurer, M. (2017). Towards a functional system architecture for automated vehicles. arXiv preprint arXiv:1703.08557.