## Slide 1: Autonomous Cyber-Physical Systems: Design and Analysis of Hybrid Systems
Spring 2018. CS 599.
Instructor: Jyo Deshmukh
Acknowledgment: Some of the material in these slides is based on the lecture slides for CIS 540: Principles of Embedded Computation taught by Rajeev Alur at the University of Pennsylvania. http://www.seas.upenn.edu/~cis540/
This lecture also uses some other sources, full bibliography is included at the end of the slides.

## Slide 2: Layout
Hybrid Systems Background
  Hybrid Process Formalization
  Stability analysis for hybrid systems
  Reachability analysis for hybrid systems
Hybrid Systems applications
  Model-based Design V
  Obstacle-avoidance for robots

## Slide 3: Hybrid Process
Inputs, Outputs, States (both continuous and discrete), Internal actions, input and output actions exactly like the asynchronous model
Continuous action/transition:
Discrete mode does not change
=
satisfies the given dynamical equation for mode
Output satisfies the output equation for mode :
At all times , the state satisfies the invariant for mode

## Slide 4: Hybrid Process
Discrete action/transition:
  Happens instantaneously
  Changes discrete mode to
  Can execute only if evaluates to true
  Changes state variable value from to
  should satisfy mode invariant of
  Some definitions make a function of and
  Output will change from to
/

## Slide 5: Executions of a hybrid process
At each cell boundary, assume that the guard is the equation of the boundary, and the reset is where
Invariant for each cell/mode is the open set enclosed by its boundaries
Suppose initial state is
(0,0)
(0,1)
(0,2)
(0,3)
(1,0)
(2,0)
(3,0)

## Slide 6: Stability of hybrid systems
Hybrid systems can have surprising results with respect to stability
No uniform method like Lyapunov analysis for analyzing all hybrid systems
Example: Piecewise Linear (PWL) Dynamical System
  Special class of hybrid system, in which each mode has linear dynamics, guards, resets are all linear/affine
  Each mode in the PWL system can have stable dynamics (by doing eigen-value analysis), but resulting hybrid system may be unstable!

## Slide 7: Example
Dynamics in each mode are stable!

## Slide 8: Simulation results
Initial State

## Slide 9: Stability analysis for hybrid systems
Two main approaches1,2:
  Find a common Lyapunov function that works for all modes
    I.e. for each mode , dynamics are , find such that: , and
    Usually hard to find a “one-size-fits-all” Lyapunov function
  Find multiple Lyapunov functions, one for each mode
    In each mode its Lyapunov function value decreases, and at the switching instant the destination mode’s Lyapunov function value does not increase
    value decreases every time mode is entered
    Finding Lyapunov functions satisfying these conditions is again hard

## Slide 10: Reachability analysis
Suppose the grid world represents the configuration space of a robot
How do we analyze: Does the robot reach the error cell?
  Easy if we have only one initial state: just simulate!
What if the initial position of the robot is not certain (could be a set)?
What if the dynamics are not certain?
(0,0)
(0,1)
(0,2)
(0,3)
(1,0)
(2,0)
(3,0)
Initial states

## Slide 11: Time-bounded Reachability Analysis
Fundamental problem for dynamical systems
Simulation:
  Given an initial condition , compute solution such that
Time-bounded Reachability:
  Given a set of initial conditions , and a time T, compute the set such that
  A useless (but correct) answer is
  How do we find a “tight” reachable set?

## Slide 12: Computing Reachable Sets3
Main idea: compute successor states
  For a given set of states,
  For a given set ,
  For a given set , compute and
Use a recurrence relation to do fixpoint computation

## Slide 13: Fixpoint computation of reachable states
Computation:
  Initialize (initial set of states)
  Recur:
  Terminate if:
    Time-bounded: when the sum of time elapsed on all continuous transitions is
Problems:
  Termination not guaranteed for general case
  is not easy to compute in general
  Error in computing can blow-up leading to answers that are too conservative
Good tools for Hybrid processes with Linear Dynamics: SpaceEx (and a few others)
Good tools for Hybrid processes with Nonlinear Dynamics: C2E2, Flow*, dReach, CORA (and a few others)

## Slide 14: Design Application: Autonomous Guided Vehicle
Objective: Steer vehicle to follow a given track
Control inputs: linear vehicle speed , vehicle angular velocity , start/stop
Constraints on control inputs:
Designer choice: only if , otherwise

## Slide 15: On/Off control for Path following
Track
When , controller decides that vehicle goes straight, otherwise executes a turn command to bring error back in the interval
Turn right
Turn left
Go straight
Stationary

## Slide 16: Design Application: Robot Coordination
Autonomous mobile robots in a room, goal for each robot:
  Reach a target at a known location
  Avoid obstacles (positions not known in advance)
  Minimize distance travelled
Design Problems:
  Cameras/vision systems can provide estimates of obstacle positions
    When should a robot update its estimate of the obstacle position?
  Robots can communicate with each other
    How often and what information can they communicate?
  High-level motion planning
    What path in the speed/direction-space should the robots traverse?

## Slide 17: Path planning with obstacle avoidance
Goal
Assumptions:
  Two-dimensional world
  Robots are just points
  Each robot travels with a fixed speed
Dynamics for Robot :
  ;
Design objectives:
  Eventually reach
  Always avoid Obstacle1 and Obstacle 2
  Minimize distance travelled
Obstacle 1
Obstacle 2

## Slide 18: Divide path/motion planning into two parts
Computer vision tasks
Actual path planning task
Assume computer vision algorithm identifies obstacles, and labels them with some easy-to-represent geometric shape (such as a bounding boxes)
  In this example, we will assume a sonar-based sensor, so we will use circles
Assuming the vision algorithm is correct, do path planning based on the estimated shapes of obstacles
Design challenge:
  Estimate of obstacle shape is not the smallest shape containing the obstacle
  Shape estimate varies based on distance from obstacle

## Slide 19: Estimation error
Robot maintains radii and that are estimates of obstacle sizes
Every seconds, executes following update to get estimates of shapes of each obstacle:
Computation of is symmetric
Estimated shape
from distance
Estimated shape
from distance
Smallest shape
bounding obstacle
Estimated radius ,
where is a constant

## Slide 20: Path planning
Choose shortest path to target (to minimize time)
If estimate of obstacle 1 intersects , calculate two paths that are tangent to obstacle 1 estimate
If estimate of obstacle 2 intersects , or obstacle 1, calculate tangent paths
Plausible paths: and
Calculate shorter one as the planned path

## Slide 21: Dynamic path planning
Path planning inputs:
  Current position of robot
  Target position
  Position of obstacles and estimates
Output:
  Direction for motion assuming obstacle estimates are correct
May be useful to execute planning algorithm again as robot moves!
  Because estimates will improve closer to the obstacles
  Invoke planning algorithm every seconds

## Slide 22: Communication improves planning
Every robot has its own estimate of the obstacle
’s estimate of obstacle might be better than ’s
Strategy: every seconds, send estimates to other robot, and receive estimates
For estimate , use final estimate =
Re-run path planner

## Slide 23: Improved path planning through communication
Old path
New path available
because estimate of obstacle 1 improved after receiving estimate from

## Slide 24: Advantage of using hybrid processes
See Fig. 9.19 in book for hybrid process for a robot
Hybrid process combines computation, communication and control
Elegant machine that exemplifies the basic operation of a cyber-physical system
Allows design-space exploration through simulations and reachability analysis
  We can check effect of parameter choices on the behavior of the system

## Slide 25: Bibliography
H. Lin and P. J. Antsaklis, "Stability and Stabilizability of Switched Linear Systems: A Survey of Recent Results," in IEEE Transactions on Automatic Control, vol. 54, no. 2, pp. 308-322, Feb. 2009.
Branicky, Michael S. "Multiple Lyapunov functions and other analysis tools for switched and hybrid systems." IEEE Transactions on automatic control 43.4 (1998): 475-482.
Talk by Goran Frehse, pdf of slides here: http://qmc.cs.aau.dk/slides/slides-frehse.pdf
SpaceEx: http://spaceex.imag.fr/
Flow*: https://flowstar.org/
dReach: http://dreal.github.io/dReach/
CORA: http://www.i6.in.tum.de/Main/SoftwareCORA