## Slide 1: Autonomous Cyber-Physical Systems: Synchronous Components: II
Spring 2018. CS 599.
Instructor: Jyo Deshmukh
Acknowledgment: Some of the material in these slides is based on the lecture slides for CIS 540: Principles of Embedded Computation taught by Rajeev Alur at the University of Pennsylvania. http://www.seas.upenn.edu/~cis540/

## Slide 2: Synchronous Reactive Component: Recap
Set of Typed Inputs, Typed Outputs, Typed State Variables, Updates
Every round: read input, update state, update output
bool in
bool out
bool x := 0
out:=x ; x:= in

## Slide 3: Today
Finish Synchronous Components
Cruise Controller Model

## Slide 4: Let’s Formalize an SRC
SRC is defined as a tuple: , where:
Symbol | Designation | Examples
 | Set of Inputs | { {}
 | Set of State Variables | {}
 | Set of Outputs | {}
 | Set of Updates | 
Symbol | Designation | Examples
 | Set of Inputs | 
 | Set of State Variables | 
 | Set of Outputs | 
 | Set of Updates | 

## Slide 5: Variables vs. Valuations
A valuation function maps each variable to some value
Input valuation maps each input to some value in the set of possible inputs, e.g.:
  if input variable is of type bool, in each round, the valuation function maps an input variable to some value in {0, 1}
  if a state variable is of type int, in each round, the state-valuation maps state variable in each round to some value in {int_min,…-1, 0, 1, .. int_max}
Let set of input, output, and state values be

## Slide 6: What are the for these SRCs?
bool in
bool out
bool x := 0
out:=x ; x:= in
bool in
int out
int y:= 0
bool z:= 0
out:=y ;
if (z==0)
y:= y + 1
else
y:= y-1
z := in
Notes: int = {int_min,..,-1,0,1,..int_max}
Q_I = {0, 1}, Q_O = {0, 1}, Q_X = {0,1}
Q_I = {0,1}, Q_X = int x {0,1}, Q_O = int

## Slide 7: Semantics of updates & initialization
Semantics of the initialization function:
  At time/round 0, maps the state variables to some specified value (or values) in
Semantics of the update function (some sequence of conditionals and assignments):
  A set of reactions where each reaction is of the form: , where is the old value of the state variables, is the new value of the state variables, is the value of the input in that round, and is the value of the output
  is a subset of

## Slide 8: Reactions for Delay
bool in
bool out
bool x := 0
out:=x ; x:= in

## Slide 9: Deterministic Component
An SRC is deterministic if:
  It has a single initial state
  Updates ensure that for every state and input , there is a unique state and output such that is a reaction
Determinism means for same input sequence, you get same state/output sequence every single time
Note:
  Nondeterminism is useful for modeling uncertainty/unknown
  It is not the same as probabilistic/random choice!

## Slide 10: Reactions for LossyDelay
Set of reactions:
bool in
bool out
bool x := 0
out:=x ;
x:= choose{in,x}
x:= choose(y,z) nondeterministically assigns x with either y or z
Motivation: Abstraction, Missing input
LossyDelay

## Slide 11: Input-Enabled Component
An SRC is input-enabled if:
  For every state and input there is some state and some output such that is a reaction
Component that is not input-enabled is making assumptions about the context in which it will be used!

## Slide 12: Not input-enabled component: missing reactions
bool in
bool out
bool x := 0
if (in==0) out:=x
Set of reactions contains only 2 reactions now!
Motivation: Blocking communication

## Slide 13: Extended State Machines
Commonly used to describe behavior of MBD models
Does this ESM remind you of something?
0
1
(in==0)?
0
(in==1)?
0
(in==1)?
1
(in==0)?
1

## Slide 14: Component Switch: What does this do?
bool press
bool out
int x := 0
bool q := 0
switch (q)
case 0: if (press==1) q:= 1
case 1: if (press==0) & (x < 10)
q:=1; x:= x+1
elseif (press==1) or ( x >= 10)
q:=0; x:= 0
end
end

## Slide 15: ESM corresponding to Switch SRC
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) & (x10) ?
q = 0 : off
= 1 : on

## Slide 16: ESM notation
Implicit variable called “mode” that is a discrete state variable over some finite enumeration. Here: {on, off}
SRC reaction may correspond to mode-switch
Each mode-switch has:
  Guard: (press==0) & (x<10) and
  Update: x:= x+1
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) & (x10) ?

## Slide 17: ESM execution
Start in mode off; initial state = (off,0)
Sample executions:
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?

## Slide 18: ESM transitions could be nondeterministic!
off
on
(press==0)?
(press==1)?
(press==0) & (x10) ?
0
(press==1) or (x10) ?

## Slide 19: SRC: Finite-state Components
bool in
bool out
bool x := 0
out:=x ; x:= in
bool in
int out
int y:= 0
bool z:= 0
out:=y ;
if (z==0)
y:= y + 1
else
y:= y-1
z := in
Component is finite state if all variables are over finite types
FS
Not FS!

## Slide 20: Combinational component
Combinational components have no state variables
bool
bool out
out≔
Hardware logic gates are combinational!

## Slide 21: Event-triggered Components
SRC: each component participates in each round
Synchronous assumption can become cumbersome if we want some components to not participate in some rounds
Hack: Event-triggered component
Event is a special input/output variable, which can be absent or present
Event variable has value only if it is present
Syntax:
e? | True if e is present
e!a | e gets the value of the assignment a

## Slide 22: Event-triggered Copy
bool in
event(bool) flag
bool x := 0
if clk? then
flag!x; x:=in
event(bool) clk

## Slide 23: Event-triggered Components
No need to execute in a round where triggering events are absent
event(bool) sec
event(bool) min
nat x := 0
if sec? then
x:=x+1;
if (x==60)
min! 1;
x:=0
end
end

## Slide 24: Putting together a complex SRC from smaller SRCs
Main rule: can share input variables, but states and output variables need to be distinct
Must be careful to rename states and output variables when “instantiating” an SRC
bool in
bool out
bool x := 0
out:=x ; x:= in
Delay
bool in
bool temp
bool x1 := 0
temp:=x1 ; x1:= in
Delay1

## Slide 25: Parallel Composition
Gives semantics of connecting two SRCs
DoubleDelay = Delay1 || Delay2
Rules for composing components: define initialization, input/output/state variables and reactions in terms of components
bool out
Delay2
bool in
bool temp
Delay1

## Slide 26: Compatibility of Components
Can have common input variables
Cannot have common output variables
  One component: one output
Cannot have common state variables
  Each component knows only its state. Can rename state variables to avoid conflicts
Input variable of one can be output of another

## Slide 27: Defining Outputs
Outputs of DoubleDelay are {temp, out}
  (Default is to make every output available to the external world)
If C1 has outputs and C2 has outputs , then the parallel composed SRC has outputs
bool out
Delay2
bool in
bool temp
Delay1

## Slide 28: Defining Inputs
Input of DoubleDelay is {in}. Note temp is not an input of the product
If C1 has inputs and outputs and C2 has inputs and outputs , then the parallel composed SRC has inputs
  A variable is an input if it is not some components output
bool out
Delay2
bool in
bool temp
Delay1

## Slide 29: Defining states
State variables of DoubleDelay :{
C1’s state variables : and C2’s state variables: then (C1||C2)’s state variables:
A state of the parallel composed SRC is a pair where is a state of C1 and is a state of C2.
States of composed SRC take values in . So if C1 has states and C2 has states, C1 || C2 has states.
bool out
Delay2
bool in
bool temp
Delay1

## Slide 30: Defining Initialization
Initialization code can be interpreted to have run in any order
If Delay1’s init code is: , and Delay2’s init code is , then DoubleDelay’s init code is
In this example, initial state variable value is (0,0)
bool out
Delay2
bool in
bool temp
Delay1

## Slide 31: Reactions
Reactions are consistent with executing update statement of Delay1 before that of Delay2
If components not connected acyclically, composition (e.g. feedback) becomes problematic!
bool out
Delay2
bool in
bool temp
Delay1

## Slide 32: Cruise Controller Example
CruiseController
event second
event cruise
event inc
event dec
Clock
Sensor
event rotate
Display
nat speed
event(nat) cruiseSpeed
ThrottleController
event(real) F
Driver Inputs

## Slide 33: Sensors
Rotation Sensor: Wheel speed sensor or vehicle speed sensor
Type of a tachometer
Counts number of rotations per second and as the wheel radius is known, can compute the linear speed of the car
(From Porter and Chester Institute slides on Google Image Search)

## Slide 34: Actuator
ThrottleController is an actuator that gets a force/torque required to adjust the throttle plate which leads to tracking the desired speed
CruiseController
event second
event cruise
event inc
event dec
Clock
Sensor
event rotate
Display
nat speed
event(nat) cruiseSpeed
ThrottleController
event(real) F

## Slide 35: Decomposing CruiseController further

## Slide 36: MeasureSpeed SRC
event rotate
nat speed
nat count := 0, s:=0
if rotate?
count:=count + 1;
if second?
s:= round( K* count);
count:=0;
speed:=s
MeasureSpeed
event second

## Slide 37: Next time
Asynchronous Components, Timed Components