## Slide 1: Autonomous Cyber-Physical Systems: Path Planning
Spring 2019. CS 599.
Instructor: Jyo Deshmukh

## Slide 2: Decision-making hierarchy
Route Planning
Behavioral Planning
Lane following
Lane changing
Adaptive cruising
Intersection negotiation
Collision avoidance
Trajectory planning/Motion planning
Low-level Feedback control
Road topology, network
Perception layer outputs
Estimated pose and free space
Vehicle state estimates
User-specified
destination
Sequence of way-points
Motion specification
Reference path
Steering and throttle commands

## Slide 3: Route planning
Represent road network/topology as a directed graph
  Nodes represent way-points
  Edges represent a cost of traveling between nodes
Cost can represent time, distance, fuel economy, a weighted combination of some of these, etc.
Simplest solutions based on Dijkstra’s shortest-path or A* search algorithms
  In practice, these do not scale well
  Lots of different algorithms proposed in the literature5

## Slide 4: Dijkstra’s Shortest path algorithm
ShortestPath (Graph G(V, E), src)
  ; ;
A
C
D
E
F
B
3
2
6
6
5
5
1
5
 | A |  | B |  | C |  | D |  | E |  | F |  | Q
1 |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  | 3 | A | 6 | A | 6 | A |  |  | 
3 |  |  |  |  | 3 | A | 6 | A | 5 | C | 8 | C | 
4 |  |  | 10 | E | 3 | A | 6 | A | 5 | C | 8 | C | 
5 |  |  | 10 | E | 3 | A | 6 | A | 5 | C | 8 | C | 
6 |  |  | 9 | F | 3 | A | 6 | A | 5 | C | 8 | C | 
7 |  |  | 9 | F | 3 | A | 6 | A | 5 | C | 8 | C | 
 | A |  | B |  | C |  | D |  | E |  | F |  | Q
1 |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  | 3 | A | 6 | A | 6 | A |  |  | 
3 |  |  |  |  | 3 | A | 6 | A | 5 | C | 8 | C | 
4 |  |  | 10 | E | 3 | A | 6 | A | 5 | C | 8 | C | 
5 |  |  | 10 | E | 3 | A | 6 | A | 5 | C | 8 | C | 
6 |  |  | 9 | F | 3 | A | 6 | A | 5 | C | 8 | C | 
7 |  |  | 9 | F | 3 | A | 6 | A | 5 | C | 8 | C | 

## Slide 5: Dijkstra’s shortest path algorithm
Computes for each node in the graph, the shortest path from the source to that node
Classic example of a dynamic programming algorithm
Original algorithm runs in
Optimization using Fibonnaci Heaps allows complexity
Does not work for graphs with cycles or negative weights!
  Bellman-Ford algorithm for graphs with negative weights and cycles (but no negative cycles)
  Floyd-Warshall for finding shortest paths between all pairs of nodes

## Slide 6: Behavior planning
Navigate selected route while interacting with traffic participants (pedestrians, bicycles, other cars).
Behavioral layer responsible for selecting appropriate driving action based on perceived mode (as dictated by other participants, road conditions, etc.)
Finite State Machine-based approach:
  Model driving contexts and behaviors as finite sets, and use finite state machines to represent possible behaviors.
  Planning then becomes a problem of choosing appropriate transitions that ensure a desired behavior.
  Can view this is a 2-player game between the car’s controller (player 1) and the environment (player 2). Game-theoretic approaches for FSMs can identify winning strategies for the controller.

## Slide 7: Behavioral planning under uncertainty
FSM-based view may not adequately address uncertainty
Uncertainty exists in the intention of traffic participants
Intention prediction of cars, bicycles, pedestrians has been researched
  Techniques based on Gaussian mixture models
  Switching linear dynamical and stochastic systems
  Gaussian Process Regression
A big new push is probabilistic planning formalisms using Markov Decision Processes such as Partially Observable Markov Decision Processes
We will learn about MDPs/PoMDPs in the lecture on reinforcement learning

## Slide 8: Motion planning
Behavior plan decides a high-level set of maneuvers (e.g. cruise-in-lane, turn right, turn left, etc.)
This plan needs to be translated into a reference path or a reference trajectory to be followed by the vehicle.
Motion planning computes a feasible reference plan that respects feasibility (according to vehicle dynamics), obstacle avoidance, while optimizing certain costs (e.g. maximizing comfort, minimizing battery usage, etc.)
Popular approaches
  Variational methods from nonlinear optimal control
  Graph-search approaches using discretization of the state-space
  Incremental tree-based methods

## Slide 9: Path planning vs. Trajectory planning
Path planning:
  Simply provides a parametric function
    is the configuration space or state-space of the vehicle
    gives the initial configuration, and gives the final configuration, and for all intermediate , gives the intermediate configurations
  May not include a velocity profile or those for other states, but delegates this to lower-level control
Trajectory planning: Is aware of vehicle dynamics and can account for dynamic obstacles

## Slide 10: Trajectory planning
Defines a parametric function , where
  is the planning horizon, and is the set of configurations
  precisely describes how the vehicle’s behavior evolves in configuration space at each time
Trajectory planning is a more nuanced version of path planning

## Slide 11: Trajectory planning setup
: set of all continuous functions from to
Let , then:
  (where is a set of initial configurations/states)
  (where is a set of goal states)
Set of all allowed states at time denoted as
encodes holonomic constraints
  A constraint is holonomic if you can express it as , where the ’s are coordinates, i.e. constraint depends only on spatial configuration
  Holonomic constraints can encode path constraints, and dynamic and static obstacles

## Slide 12: Trajectory planning setup continued
is a differential constraint specifying constraints on smoothness of the path, velocity, acceleration, jerk constraints etc.
is a cost functional mapping any trajectory to some cost in
Optimal trajectory can be stated as follows:

## Slide 13: Trajectory planning setup continued
Trajectory planning in dynamic environments and static path planning are both PSPACE-hard problems
  At least as complex as checking SAT of a quantified Boolean formula (QBF)
  Example QBF formula:

## Slide 14: Variational methods
Rely on results from nonlinear continuous optimization
We transform the trajectory optimization to the following standard form:
Standard trick to go from constrained to unconstrained optimization is to introduce penalty functions
  Penalty method:
  Barrier function method:
  ()

## Slide 15: Variational methods
Common to use logarithmic barrier functions with Newton-like iterative methods
One problem: Trajectory space is infinite-dimensional. Solution:
  Direct methods:
    Restrict to finite-dimensional subspace, , where are some basis functions (e.g. piecewise linear interpolation uses PWL basis functions)
    Requires numerical integration approximations for the trajectory combined with optimizers like conjugate gradient descent
  Indirect methods: use Pontryagin’s minimum principle that gives optimality conditions for trajectory optimization problem
    Requires solving boundary-value problems of ODEs, that can be approximated numerically

## Slide 16: Graph-search-methods
Variational methods may get stuck in local optima, graph-search methods try to do global search
Configuration space is represented as a graph , where is a set of selected discrete configurations, and is a set of edges, where each edge is labeled by the path segment that the edge represents.
  If , then and
Feasible path can be found by concatenating feasible edges
Does require discretization of the configuration/state space!
  Hand-crafted lane graphs2
  Geometric representations
  Sampling-based discretization

## Slide 17: Some geometric representations3
Voronoi diagrams
Occupancy Grid Map
Cost Map
State Lattice
Driving Corridors
Several nice results or path planning using geometric representations, but usually computationally expensive!

## Slide 18: Sampling-based methods
Typical constraints (differential, holonomic) are usually very difficult to obtain at real-time through sensors
Sampling-based methods explore reachability of free configuration space by trying to apply controls (steering) and checking for collisions
Main purpose of these methods is to construct a roadmap, and use it for planning
Steering functions:
  Random : returns a path obtained by applying a random steering command
  Heuristic: tries to guide vehicle from point to point
  Exact: computes exact path that takes vehicle from to
  Optimal: Returns an optimal exact path

## Slide 19: Probabilistic Roadmap (PRM) Construction
for
  for
    if
    endif
  end
End
return
Sample:
Return points on a grid
Random samples
Interesting:
-nearest neighbors using appropriate distance function
Points within a ball of radius around
Trajectory plan: Use Dijkstra’s shortest-path algorithm on the resulting roadmap

## Slide 20: Heuristic search A*
Once we have a roadmap, how do we find the best path in the roadmap?
Dijkstra’s shortest path algorithm: uses best first search to build a tree representing shortest paths from a given source to all other vertices in the graph
We typically need a path to only a single vertex (in the goal set), in this case a heuristic can be used to guide the search process
Most prominent heuristic search algorithm is A*
Shown to be optimally efficient if heuristic function is admissible (never overestimates the cost)

## Slide 21: How A* works
It constructs a tree of paths starting from the initial node, expanding paths one step at a time, till one of the path reaches the goal
In each iteration, A* determines which of its partial paths to expand based on an estimate of the cost. It selects the path that minimizes , where, . Here, = cost of path from start node to , and is an estimate of the cheapest cost to go from to the goal
Heuristic function is problem-specific. For the heuristic to be admissible, it should never over-estimate actual cost to get to the goal
Dijkstra’s shortest path is a special case of A*, where

## Slide 22: A* implementation
A* (Graph G(V, E), )
  // newly discovered nodes, not yet explored
  // already evaluated nodes
  // best predecessor node so far
  // cost of reaching from
    // estimate of reaching from via
  ;
  ;

## Slide 23: Weighted A*
Admissibility criterion forces A* to inspect all equally promising paths to find the optimal
Approximate shortest paths can be found by relaxing the admissibility criterion (i.e. the function)
  This guarantees that the path found is no worse than times the optimal path
Weighted A* variants involve defining a heuristic that is a function of . E.g. static weighted A* uses

## Slide 24: Many variants of A*
Real-time re-planning: D*, Focused D*, D* Lite: recompute shortest path anytime the underlying graph changes, making use of results from previous search
Anytime search algorithms: Quickly find a (possibly sub-optimal) path first, and continue to improve the solution if there is more computational time
  Anytime A*: weighted heuristic that continues searching using cost of previously identified path as upper bound and admissible heuristic as lower bound
  Other variants such as Anytime Repairing A*, Anytime Dynamic A* etc.

## Slide 25: Rapidly Exploring Random Trees (RRTs)
RRT one of a family of algorithms based on incremental sampling, i.e. when you do not want to a priori build the entire roadmap
Also known as single-query PRMs
Very fast algorithm, allows on-the-fly construction of paths
// is a tree
for
// Find point in that is closest to
// Find control that gets you closest to from
end
Plan = Path from to s.t.

## Slide 26: RRT in action
Target
Sample goal
Select closest neighbor
Find collision-free control
Obstacle
Target
Obstacle
Target
Obstacle

## Slide 27: Problems with RRT
Suppose you are given a function that assigns costs to paths
RRT solution is usually far from optimal
Karaman & Frazzoli (2010) showed that probability of RRT converging to an optimal solution is 0
First alternative: RRG (Rapidly exploring Random Graph)
  Connects to the new sample all vertices within some distance to it
  Can create graphs with cycles
  Improves optimality: probability of RRG converging to an optimal solution is 1

## Slide 28: Many variants of PRMs and RRTs
There are many variants that exist: RRT* (rewires the tree as better paths are found), PRM*, etc.
Some of them add optimality criteria such as costs on edges
Algorithms differ in the underlying structure maintained: PRM (forest), RRT (tree), RRG (graphs with possible cycles), RRT* (acyclic graphs) etc.
There are two key considerations:
  Probabilistic completeness: given infinite time, will the procedure identify a path to the goal set
  Asymptotic optimality: does the optimal path found by the algorithm converge to the actual optimum in the limit

## Slide 29: Combining RRTs with STL
Define path planning objectives in STL
Define robustness of STL on partial trajectories
Use RRT to explore the search space
When selecting nearest neighbors of the goal point, select ones with high robustness
Allows path-planning with STL objectives!
Combining RRTs with LTL objectives has been extensively studied in the literature

## Slide 30: Bibliography
Pendleton, Scott Drew, Hans Andersen, Xinxin Du, Xiaotong Shen, Malika Meghjani, You Hong Eng, Daniela Rus, and Marcelo H. Ang. "Perception, planning, control, and coordination for autonomous vehicles." Machines 5, no. 1 (2017): 6.
Most material in this lecture is from this paper: Paden, Brian, et al. "A survey of motion planning and control techniques for self-driving urban vehicles." IEEE Transactions on Intelligent Vehicles 1.1 (2016): 33-55. https://arxiv.org/pdf/1604.07446.pdf
Katrakazas, C., Quddus, M., Chen, W. H., & Deka, L. (2015). Real-time motion planning methods for autonomous on-road driving: State-of-the-art and future research directions. Transportation Research Part C: Emerging Technologies, 60, 416-442.
https://en.wikipedia.org/wiki/A*_search_algorithm
Bast, D. Delling, A. Goldberg, M. Müller-Hannemann, T. Pajor, P. Sanders, D. Wagner, and R. F. Werneck, “Route planning in transportation networks”, https://arxiv.org/pdf/1504.05140.pdf