## Slide 1: Autonomous Cyber-Physical Systems: Verification Basics + V2X + Wrap-up
Spring 2019. CS 599.
Instructor: Jyo Deshmukh

## Slide 2: Safety Requirements
A safety requirement states that a system always stays within the set of good states (i.e. nothing bad every happens)
Examples:
  Collision avoidance: the distance between a car and a pedestrian is always greater than a threshold
  Patient’s blood glucose never drops below 80 mg/dL
  Maximum temperature specification on the battery is not exceeded
Safety requirements can be formalized using transition systems

## Slide 3: Transition System
Transition System is a tuple
  : Set of State Variables over finite or infinite domains
  : Function mapping to initial values
  : Transition description giving code to update variables in
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?

## Slide 4: Transition System
Semantics:
  Each combination of values assigned to state variables can be interpreted as a state. : set of all possible states (could be an infinite set)
  : Finite or infinite set of initial states which is a subset of
  : Finite or infinite set of transitions, which is a subset of
Values to input variables are chosen nondeterministically
  Why? This is an abstraction technique (i.e. making something less concrete)
  We are interested in making sure that no matter what input value, the TS has desirable behavior

## Slide 5: Example of a TS
: { mode, x }
Semantics:
: { mode off, x 0 }
has an infinite number of transitions
  (off, 0) (off, 0)
  (off, 0) (on, 0)
  (on, n) (on, n+1) if n < 10
  (on, n) (off, 0) otherwise
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?

## Slide 6: Transition Systems and state
All kinds of components (synchronous, asynchronous, timed, hybrid, continuous components have an underlying transition system
State in the transition system underlying a component captures any given runtime configuration of the component
Continuous components, Timed Processes, Hybrid Processes in general, have infinite number of states

## Slide 7: Example transitions for TS
(off,0)
(on,0)
(on,1)
(on,2)
(on,100)
(off,42)
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?
(on,42)

## Slide 8: TS describes all possible transitions
(off,0)
(on,0)
(on,1)
(on,2)
(on,100)
(off,42)
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?
(on,42)
Transitions indicated as dotted lines can’t really happen in the component
But, the TS will describe then, as the states of the TS are over!

## Slide 9: Reachable states of a modified switch TS
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?
(off,0)
(on,0)
(on,1)
(on,2)
(on,100)
(off,42)
(on,42)
Reachable states and transitions

## Slide 10: Reachability
A state of a transition system is reachable if there is an execution starting in some initial state that ends in .
Algorithm to compute reachable states from a given set of initial states (just BFS):
Procedure ComputeReach(TS)
  , k:=1;
  While
  Temp :=
  ForEach
  If () Temp := Temp
  EndForEach
  Temp,
  EndWhile
  Return
  EndProcedure

## Slide 11: Desirable behaviors of a TS
Desirable behavior of a TS:
  Defined in terms of acceptable (finite or infinite) sequences of states
  If all unacceptable sequences of a TS are finite in length, then the property encoding acceptable behavior is called a safety property
Safety property can be specified by partitioning the states into a safe/unsafe set
  , ,
  Any finite sequence that ends in a state is a witness to undesirable behavior, or if all (infinite) sequences starting from an initial state never include a state from , then the TS is safe.
  In other words, to get a proof of safety, do reachability computation, and if ComputeReach(TS) = , then the TS is safe

## Slide 12: Safety invariants
An invariant is a Boolean expression over the state variables of a TS
A property is called an invariant of TS if every reachable state of TS satisfies
An invariant is a safety invariant if
Examples of invariants for modified switch:
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?

## Slide 13: Safety invariants
Examples of non-invariants:
Suppose, , and
  Then, we can verify that is a safety invariant for modified switch: proof towards the end
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?

## Slide 14: Proving that something is an invariant
Given TS and a property , prove that all reachable states of TS satisfy
Recall ComputeReach(TS), it actually gives an inductive definition of reachable states
  All states specified by are reachable using 0 transitions
  If a state is reachable using transitions, and is a transition in , then is reachable using transitions
  Reachable = Reachable using transitions for some

## Slide 15: Inductive Safety Proof
Given TS and a property , prove that all reachable states of TS satisfy
Base case: Show that all initial states satisfy
Inductive case: assume state satisfies , then show that if , then must also satisfy
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?

## Slide 16: Inductive Invariant
A property is an inductive invariant of a transition system TS if
  Every initial state satisfies
  If any state satisfies , and , then satisfies
By definition, if is an inductive invariant, then all reachable states of TS satisfy , and hence it is also an invariant

## Slide 17: Proving inductive invariants: I
Consider transition system TS given by
  :
  : if then (else remains unchanged)
Is an inductive invariant?
Base case: is zero, so is trivially satisfied

## Slide 18: Proving inductive invariants: I
Inductive case:
  Pick an arbitrary state (i.e. arbitrary value for state variable ), say
  Now assume satisfies , i.e.
  Consider the transition, there are two cases:
    If , then after the transition, and
    If , then (because guard is not true), which is .
  In either case, after the update
  So is an inductive invariant, and the proof is complete
  :
  : if then

## Slide 19: Proving inductive invariants: II
Consider transition system TS given by
  : ,
  : if then (else remain unchanged)
Is an inductive invariant?
Base case: Initial state is (), so is trivially satisfied

## Slide 20: Proving inductive invariants: II
Inductive case:
  Pick an arbitrary state (i.e. arbitrary value for state variable ), say
  Now assume satisfies , i.e.
  Consider the transition if then
    What if )? Clearly, does not satisfy !
  So is not an inductive invariant for TS, and the proof fails

## Slide 21: Proving inductive invariants: III
Consider transition system TS given by
  : ,
  : if then (else remain unchanged)
Is an inductive invariant?
Base case: Initial state is (), so is trivially satisfied

## Slide 22: Proving inductive invariants: III
Inductive case:
  Pick an arbitrary state (i.e. arbitrary value for state variable ), say
  Now assume satisfies , i.e. and
  Consider the transition if then , else
  Now, if , because , , and thus . Thus, is satisfied
  The else case is trivially satisfied
  So in either case, holds
So, is an inductive invariant!

## Slide 23: How do we prove safety invariants?
To establish that is an invariant of TS:
Find another property such that
  (i.e. every state satisfying must satisfy )
  is an inductive invariant
    Show initial states satisfy
    Assume an arbitrary state satisfies , consider any state such that , then prove that satisfies
This is a sound and complete strategy for establishing safety invariants

## Slide 24: Soundness and Completeness
Formal system: a set of axioms, a grammar for specifying well-formed formulas, and a set of inference rules for deriving new true formulas from axioms
Sound: Starting from the axioms and using inference rules of the formal system, we cannot arrive at a formula that is equivalent in meaning to false.
Complete: Proof system is complete with respect to a property if every formula having that property can be derived using the inference rules
Proof rule for proving invariants is sound and complete:
  Sound: It is a correct proof technique
  Complete: If is an invariant, there is some stronger inductive invariant satisfying inductive conditions that we can find

## Slide 25: Safety Proof for Switch
Let’s try the inductive invariant:
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?
Base case: trivially satisfies
Inductive hypothesis: assume that a state satisfies
Inductive step: prove that any s.t. satisfies
  Case I:
    = [trivial]
    = [satisfies second conjunct in ]
  Case II:
    if , this implies that , so satisfies
    otherwise, this again implies that satisfies
So is an inductive invariant
Further, (note that every state satisfying will satisfy )
So is an invariant of the TS!

## Slide 26: Safety verification using barrier certificates
Barrier certificate: safety invariant for a continuous dynamical system
It establishes an invisible barrier that trajectories of a system cannot cross
  (think of it as a force-field)
Reasoning very similar to that of an inductive invariant
  Establish that the initial states all lie within the barrier
  Establish that the unsafe states are all outside the barrier
  Show that the next states for all states on the barrier are inside the barrier

## Slide 27: Strict barrier certificate
Given system
Function that serves as a classifier between good and bad states
Barrier conditions:
  (The last condition models the barrier pushing the system back!)
Unsafe
Initial

## Slide 28: Example
  Initial state set:
  Unsafe set:
Barrier:
  From plot:
    for initial states, ,
    for unsafe states,
Unsafe
Initial
Barrier

## Slide 29: Example
Finally, =
  =
    =
    =
From the plot, the above function is always negative for values of where
Barrier

## Slide 30: Time-bounded Reachability
Verification basics and Hybrid Systems lecture: reachability analysis using a “fix-point based algorithm”
  uses a breadth-first approach to compute reachable states over an infinite time-horizon
Barrier certificates: also provide infinite time safety results, but require manual ingenuity in coming up with a barrier; difficult to do for hybrid/nonlinear systems
Time-bounded reachability: Starting from some initial state in a given set of initial states, does the system behavior ever reach an unsafe state within a given time bound?

## Slide 31: Problem definition
Let be the solution trajectory of a given dynamical system (could be nonlinear, hybrid, timed, …) when the system starts in initial state
Time-bounded reachability: Prove that:
Counterexample to time-bounded reachability shown below
Unsafe
?
Trajectory segment with unsafe states
Trajectory segment with safe states

## Slide 32: Solutions to time-bounded reachability
To solve time-bounded reachability exactly:
  Compute set of all states reachable from :
  Check if is empty
  Challenge: computing is very hard (even for the simplest case of general linear dynamical systems)
Instead, we focus on approximating
  Under-approximation
  Over-approximation
  Combination of both

## Slide 33: Under-approximation
When we under-approximate the set of initial states, at each time, the set of reachable states that we compute is a subset of the actual set of reachable states
Best example of under-approximation is (guaranteed) numerical simulation
  Guaranteed numerical simulation: better than numerical integration schemes as it gives bounds on error in numerical integration (e.g. VNODE)
Under-approximation is:
  Sound for bug-finding: if we find a bug, then it is really a bug
  Unsound for verification: if we do not find a bug, does not mean the system is safe

## Slide 34: Under-approximation: sound for bug-finding
The good case: under-approximation found a trace that contained unsafe states – we found a bug in the system!

## Slide 35: Under-approximation: unsound for verification
The bad case: under-approximation did not find a trace that contained unsafe states – we cannot conclude anything.

## Slide 36: Over-approximation
When we over-approximate the set of initial states, at each time, the set of reachable states that we compute is a superset of the actual set of reachable states
Most formal verification techniques are based on over-approximation
Over-approximation is:
  Unsound for bug-finding: if we find a bug, then it may not really be a bug
    Because of over-approximation error
  Sound for verification: if we do not find a bug, we have a proof that the system cannot reach an unsafe state in any time in

## Slide 37: Reachability for piecewise affine (PWA) systems
PWA systems are a simplification of hybrid automata
For a PWA system with modes:
  Each mode described by an affine invariant of the form
  In each mode the dynamics are described as: +
A lot of research over last 20 years on computing the set of reachable states for PWA systems
  Focus: reduce approximation error and increase scalability (in number of modes)
  Tools: PHAver, d/dt, CheckMate, SpaceEx

## Slide 38: Reachability for affine systems
Recall that for a linear system (for now assume no inputs):
Let , now is just some constant matrix
If is some polyhedral set, we can compute the exact set of reachable states for every state in at time , because is just a linear transform
Thus, we get
Could be acceptable for continuous systems: between discrete time steps, solution remains in the neighborhood of the aproximations (and we can over-estimate this neighborhood numerically)

## Slide 39: Problem for CPS (hybrid systems)
Controller may be event-triggered, where it detects the level of a certain physical quantity, and based on that changes mode of operation
An event firing between consecutive time steps could take the PWA system in a different mode!
We need to account for what may happen between time-steps
This is done by covering the reach-sets computed at times and by a shape that includes both
Lots of research done on which shape is the best, and different shapes have different tradeoffs
  Ellipsoids, Zonotopes, Support Functions
  SpaceEx tool uses support functions, and is pretty accurate for reasonably sized PWA systems now
Wrong!

## Slide 40: Reachability for nonlinear systems
Not all systems can be modeled as PWA!
Nonlinear systems:
  Approach I: first PWA-ize the system, then do reachability. Drawback: Error encountered during PWA-ization accumulates
  Approach 2: use more interesting models such as Taylor models (based on Taylor series representations): used in tool Flow*
  Approach 3: throw the problem at a powerful nonlinear SMT solver: used in tool dReach

## Slide 41: Combining under and over-approximations
Also known as simulation-guided reachability analysis
Main idea:
  Sample some initial states, perform simulations starting from these states
  Use “continuity”-like arguments to bloat the trajectories in a sound manner
  If bloated trajectories cover initial state space, go to step 4, if not go back to step 1
  If bloated trajectories do not intersect unsafe set, conclude system is safe. If bloated trajectories intersect unsafe set, try to refine bloated trajectories to check if there is a true counterexample

## Slide 42: Simlulation-guided reachability depiction
Unsafe
Initial
Simulation Trace up to time T
Reach-Tube up to time T

## Slide 43: Secret sauce: how to bloat
Main idea: Solutions of ODEs are “sensitive” to their initial conditions
Such sensitivity gives an estimate on how far two trajectories can go if they start apart
A key notion is a discrepancy function that bounds how far trajectories can grow
Obtaining a that shows trajectories remain bounded within some reasonable factor of the distance between their initial conditions is very useful
  We only simulate from , and we know how all neighbors of will behave!
Technique implemented in tool C2E2

## Slide 44: Bibliography
Breach : https://link.springer.com/chapter/10.1007/978-3-642-14295-6_17
Prajna, S., & Jadbabaie, A. (2004, March). Safety verification of hybrid systems using barrier certificates. In International Workshop on Hybrid Systems: Computation and Control (pp. 477-492).
Duggirala, Parasara Sridhar, et al. "C2E2: a verification tool for stateflow models." International Conference on Tools and Algorithms for the Construction and Analysis of Systems.
Frehse, Goran, Colas Le Guernic, Alexandre Donzé, Scott Cotton, Rajarshi Ray, Olivier Lebeltel, Rodolfo Ripado, Antoine Girard, Thao Dang, and Oded Maler. "SpaceEx: Scalable verification of hybrid systems." In International Conference on Computer Aided Verification, pp. 379-395. Springer, Berlin, Heidelberg, 2011.
Chen, Xin, Erika Ábrahám, and Sriram Sankaranarayanan. "Flow*: An analyzer for non-linear hybrid systems." In International Conference on Computer Aided Verification, pp. 258-263. Springer, Berlin, Heidelberg, 2013.
Frehse, Goran. "PHAVer: Algorithmic verification of hybrid systems past HyTech." International workshop on hybrid systems: computation and control. Springer, Berlin, Heidelberg, 2005
Asarin, E., Dang, T., & Maler, O. (2002, July). The d/dt tool for verification of hybrid systems. In International Conference on Computer Aided Verification (pp. 365-370). Springer, Berlin, Heidelberg.
Fan, Chuchu, Bolun Qi, Sayan Mitra, Mahesh Viswanathan, and Parasara Sridhar Duggirala. "Automatic reachability analysis for nonlinear hybrid models with C2E2." In International Conference on Computer Aided Verification, pp. 531-538. Springer, Cham, 2016.
Donzé, Alexandre, and Oded Maler. "Systematic simulation using sensitivity analysis." In International Workshop on Hybrid Systems: Computation and Control, pp. 174-189. Springer, Berlin, Heidelberg, 2007

## Slide 45: V2V communication
Single hop: Vehicle communicates directly with another vehicle
Multi-hop: Vehicle uses intermediate nodes for communication
V2V has been used for safety:
  Stopped vehicle or obstacle avoidance on highways
  Merging assistance from a slow incoming lane to a crowded road
  Intersection safety and collision warning systems
Consensus around DSRC (Dedicated Short-Range Communication) using IEEE 802.11p/WAVE standards
Potential applications:
  multi-vehicle sensor fusion for localization, mapping
  Platooning and energy management

## Slide 46: V2I communication
Vehicle to Infrastructure communication
Applications:
  Electronic Toll Collection
  Intersection safety with Smart traffic lights
    (Cooperative Intersection Collision Avoidance System)
  Better route-planning with a traffic-congestion aware cloud system
  Computing on the cloud for complex optimization situations

## Slide 47: Cooperative Adaptive Cruise Control (CACC)
Used for platoons of vehicles (e.g. trucks)
Several goals:
  Improve safety
  Improve traffic flow dynamics by damping disturbances (new cars, braking, bumps in the road)
  Increasing highway capacity by shorter following gaps
  Saving energy and pollution through aerodynamic drafting
  Improving driver comfort and convenience

## Slide 48: CACC with V2X
Many V2V variants based on where information comes from
  Immediate leader or/and follower or/and the overall Platoon Leader or/and any vehicle in range
Simplest scheme: Pairwise sharing between vehicle and immediate leader
V2I schemes: communicate with traffic management center/roadside devices either statically or dynamically
  Can help with intersections
  Can help with green-driving or eco-driving

## Slide 49: CACC uses different gap regulation strategies
Constant clearance or constant distance gap (CDG)
  Separation does not change with vehicle velocity
  Gives experience of mechanical linkage between vehicles
  Requires more formal platoon architecture and tight communication between platoon leader and followers
  Communication interruption can cause safety hazards
  Need larger gaps to ensure safety of platoon
  (Emergency brake by leader can cause domino effect)

## Slide 50: Constant Time Gap
Resembles how normal human drivers drive (except on 110 in LA )
Distance between vehicles is proportional to their speed + a small fixed offset distance
E.g. doubling of speed causes doubling of gap between vehicles
Time gap criterion described in terms of time between rear bumper of leading vehicle and front bumper of trailing vehicle pass a fixed point on te roadway
Often described as headway or time headway
Vehicles in CTG CACC are often called a “string of vehicles” rather than platoon

## Slide 51: Autonomous Intersection Management
AIM protocol and its variants proposed based on V2I communication
Main idea :
  Each car equipped with a driver agent
  Each intersection equipped with an intersection manager
  Driver agents call ahead to reserve space-time in an intersection
  Intersection manager decides to grant or reject reservation requests according to an intersection control policy

## Slide 52: AIM protocol4
Approach vehicle announces arrival to manager
Vehicle indicates its size, predicted arrival time, velocity, acceleration, arrival and departure lanes
Intersection manager simulates vehicle’s path through the intersection, checking for conflicts with paths of previously processed vehicles
If there are no conflicts, issues a reservation
It is the vehicle’s responsibility to arrive at and travel through the reserved space-time block within some range of error tolerance
In case of conflict, intersection manager suggests an alternate later reservation
Car enters intersection only if reservation successful
Upon leaving intersection, car conveys successful passage to the manager

## Slide 53: Intersection control policies
Divide intersection into grid of reservation tiles

## Slide 54: Many AIM5 variants with different concerns
Decentralized (vehicles coordinating among themselves) vs. Centralized (manager)
Deliberative (planning entire trajectories) vs. reactive (planning trajectories in real-time)
Robust (Safety margins) vs. efficient (more throughput at the intersection)
Cooperative (optimizing overall traffic flow) vs. Egoistic (optimizing your own speed/time)
Homogenous (all vehicles treated the same) vs. Heterogeneous
Modeling AIM: asynchronous, timed, & hybrid process models used!

## Slide 55: Collaborative merge
Purpose: allow vehicles merging onto a freeway from a ramp to do so in safe fashion
Can be formulated as a specific case in autonomous intersection management
Specialized approaches based on highway ramp metering have existed for some time (these do not utilize V2V capability, and do not guarantee safety)

## Slide 56: Collaborative merge
Region at center of intersection called merging zone with length
Control zone of length where vehicles can communicate
Each vehicle modeled with simple second-order dynamics (position, velocity, acceleration)
Centralized solution based on layered control approaches

## Slide 57: Two-layered control approach for merging
Centralized approach (V2I only)
First layer
  Assumes each vehicle is traveling at constant speed
  Computes time for each vehicle to merge into the control zone based on this assumption
Second layer
  Determines conflicts in merging sequence
  Computes required acceleration value based on heuristic rules
Generalization with different layers of control has been proposed
Optimization: minimizing vehicle overlap (crash!) and travel time

## Slide 58: Decentralized approach
Virtual vehicle mapped onto the freeway before actual merging occurs
Allows vehicles to perform smoother and safer control actions
Uses slot-based traffic management (vehicles drive into a virtual slot)
Vehicles use V2V and V2I communication with vehicles in range
Other approaches based on MPC also exist

## Slide 59: Design challenges Course Concepts
Modeling protocols, decision layer components
  Synchronous and Asynchronous processes
  Understanding system-level safety using synchronous and asynchronous composition
  Verification using Model Checking, Inductive Invariants
  Liveness properties with LTL, CTL
  Model-based and Scenario-based Testing approaches

## Slide 60: Design challenges Course Concepts
Modeling Controllers, Path planning
  Timed and Hybrid Processes, Dynamical Systems
  Markov Decision Processes & Markov Chains
  Verification using Model Checking, Inductive invariants, safety certificates (barrier certificates), Liveness checking with LTL, CTL, STL
  Testing using Falsification-based approaches
  Software synthesis using Temporal Logic-based approaches, reinforcement learning

## Slide 61: Design Challenges Course Concepts
Reasoning about environments, physical processes to be controlled
  Dynamical systems models, hybrid processes
  Signal Temporal Logic as a way to express Cyber-Physical systems specifications
  Testing and Falsification approaches
  Reasoning about safety and security
  Models for perception

## Slide 62: How does everything fit together?
You want to develop a new CPS/IoT system with autonomy
Analyze its environment: model it as a dynamical system or a stochastic system (e.g. PoMDPs)
Analyze the different components required in the software stack
  Perception vs. Decision/Planning vs. Control
Analyze what models to use for the control algorithms
  Choices are: Traditional control schemes (PID/MPC), state-machines (synchronous vs. asynchronous based on communication type), AI/planning algorithms, hybrid control algorithms, or combinations of these

## Slide 63: Safety is the key!!
Try to specify the closed-loop system as something you can simulate and see its behaviors
  Integrative modeling environment such as Simulink (plant models + software models)
  Specify requirements of how you expect the system to behave (STL, LTL, or your favorite spec. formalism)
    This step is a DO NOT MISS. It will provide documentation of your intent, and also a machine-checkable artifact
Test the system a lot, and then test some more
Apply formal reasoning wherever you can. Proofs are great if you can get them
Safety doesn’t end at modeling stage; continue reasoning about safety after deployment (through monitoring etc.)

## Slide 64: It’s been a fun class
Basics of Control
  PID, MPC, Nonlinear control, Observer design (Kalman filter)
Basics of Perception
  Vision-based systems, CNNs
Basics of Planning
  Path planning, Reinforcement learning
Basics of Security and Communicating Autonomous CPS
Models of computation
  Asynchronous, Synchronous, Timed, Hybrid Processes, Dynamical Systems, Probabilistic Models, Simulink
MODELING
AUTONOMY
Basics of Safety-Aware Mindset
Specification Languages (LTL, CTL, STL)
Falsification and Testing
Safety Invariants + Proofs
Reachability, Model Checking
SAFETY
Safe Autonomous CPS

## Slide 65: References
[1] Shladover, Steven E., et al. "Cooperative adaptive cruise control: Definitions and operating concepts." Transportation Research Record: Journal of the Transportation Research Board 2489 (2015): 145-152.
[2] ibid., https://escholarship.org/uc/item/7jf9n5wm
[3] Liang, Chi-Ying, and Huei Peng. "String stability analysis of adaptive cruise controlled vehicles." JSME International Journal Series C Mechanical Systems, Machine Elements and Manufacturing 43.3 (2000): 671-677.
[4] Stone, Peter, Shun Zhang, and Tsz-Chiu Au. "Autonomous intersection management for semi-autonomous vehicles." Routledge Handbook of Transportation. Routledge, 2015. 116-132.
[5] Qian, Xiangjun, et al. "Autonomous Intersection Management systems: criteria, implementation and evaluation." IET Intelligent Transport Systems 11.3 (2017): 182-189.
[6] de Campos, Gabriel Rodrigues, et al. "Traffic coordination at road intersections: Autonomous decision-making algorithms using model-based heuristics." IEEE Intelligent Transportation Systems Magazine 9.1 (2017): 8-21.
[7] Rios-Torres, Jackeline, and Andreas A. Malikopoulos. "A survey on the coordination of connected and automated vehicles at intersections and merging at highway on-ramps." IEEE Transactions on Intelligent Transportation Systems 18.5 (2017): 1066-1077.